## Slide 1: College of Engineering Department of Civil Engineering Spring 2021 – Learning Outcome Assessment III CE (Final Presentation) Abqaiq – Half-moon Highway Design with Reinforced Concrete Bridge Design Section
Presented by: (Group 1)
Abdullah S. Alshammari 201801677
Abdulmohsen B. Alkhalifa 201601825
Hassan A. Alhajji 201602934
Turki A.Albasha 201601658
Advisor: Dr. Mohammed Ali Khasawneh, Ph.D.
Coordinator: Dr. Andi Asiz, Ph.D.

## Slide 2
Main Project: Transportation Highway.
Introduction.
Project Description.
Traffic analysis.
Horizontal Alignment.
Vertical Alignment.
Soil Investigation.
Pavement Design.
Derange system.
Intersections Design.
Sub – Project: Precast section Bridge.
Cost estimation.
Summary & Conclusions.
References.
Outlines

## Slide 3: Introduction
Project Background.
Project Area.
Objectives:
Geometrical design of the highway.
Structural design of the pavement (including drainage).
Structural and geotechnical design of a single span RC bridge.
Cost estimation.
Project constraints.
Figure 1 - Project Location (Google Earth Pro)

## Slide 4: Introduction
Figure 2 – Methodology Procedure
Methodology

## Slide 5: Project Description
How to Select the best Alternative Path? Why?
Table 1 - Alternative selection information
Figure 3 - Alternative paths (Google Earth Pro)
Alternatives | Road length (km) | No. of Horizontal Curves | No. of Vertical Curves | Cut / Fill Net Quantity (𝐦𝟑)
Path A | 24.9 | 10 | 7 | 203934 (Fill)
Path B | 25.5 | 6 | 4 | 1559308 (Fill)
Path C | 26.2 | 5 | 6 | 279841 (Fill)

## Slide 6: Traffic Analysis
Traffic Analysis Data
Speed Design
Number of Lanes

## Slide 7: Traffic Analysis
Analysis of Traffic Data
and Calculations.
Month | No. of Weekdays In Month (days) | Total Days in Month (days) | Total Monthly Volume (vehs) | Total Weekday Volume (vehs) | Average Weekday Traffic (veh/day) | Average Daily Traffic (veh/day)
Jan | 22 | 31 | 980,483 | 552,346 | 25,107 | 31,628
Feb | 20 | 28 | 1,110,231 | 648,736 | 32,437 | 39,651
Mar | 22 | 31 | 1,109,486 | 596,254 | 27,102 | 35,790
Apr | 22 | 30 | 1,352,329 | 748,392 | 34,018 | 45,078
May | 21 | 31 | 1,458,900 | 699,837 | 33,326 | 47,061
Jun | 22 | 30 | 1,744,297 | 800,481 | 36,386 | 58,143
Jul | 23 | 31 | 1,267,345 | 822,830 | 35,775 | 40,882
Aug | 21 | 31 | 1,56,7320 | 910,271 | 43,346 | 50,559
Sep | 22 | 30 | 1,606,438 | 700,392 | 31,836 | 53,548
Oct | 22 | 31 | 999,825 | 444,372 | 20,199 | 32,252
Nov | 21 | 30 | 1,000,239 | 633,283 | 30,156 | 33,341
Dec | 22 | 31 | 932,357 | 492,774 | 22,399 | 30,076
Total | 260 | 365 | 15,129,250 | 8,049,968 | ___ | ___
Table 2 – Traffic analysis calculation

## Slide 8: Traffic Analysis
Traffic consists of different types of vehicles.
1.Passenger cars (PC)
4.PICK UP
2.JEEP MODEL
8.SMALL BUS
7.BIG BUS
5.LIGHT TRUCK
6.TRUCKS 4/14
9.TRUCKS 5/18
Note: All vehicles type pictures above are from (Freepik)
3.TRUCKS 2/6
Chart 1 - Percentage of Vehicle Type Annual
Chart: Percentages %
| PC | PICK UP | JEEP MODEL | SMALL BUS | BIG BUS | Light Trucks | Trucks (2/6) | Trucks (4/14) | Trucks (5/18)
Series 1 | 36.56 | 13.8 | 8.05 | 4.57 | 6.01 | 5.66 | 12.55 | 9.11 | 3.69
Figure 4- different types of vehicles

## Slide 9: Traffic Analysis
Design of Speed.
Upper speed (km/h) | Lower speed (km/hr) | Road degree
50 | 30 | Local
60 | 50 | Collector
100 | 80 | Arterial Highway
90 | 70 | Less disorder
60 | 50 | High disturbance
120 | 90 | Freeway
Speed (km/h) |  |  | Nature of the region
Rural road | Secondary road | Urban road | 
80 | 100 | 120 | Plain area
60 | 80 | 100 | Rolling area
Table 3 - Speed limit according to (AASHTO 2001)
Table 4- Speed with respect to the area according to (AASHTO 2001)
Accordingly, it is classified as a (Freeway) and (Urban) road. So, the designed speed = 120 km/h.

## Slide 10: Traffic Analysis
Number of Lanes.
Final Shape.
Figure 5 - Illustrating the highway diminutions (Final Shape)
Functional classification | Width (m)
Lane | 3.65
Right shoulder | 3.65
Left shoulder | 1.2
Medians | 4
Table 5- standers dimensional according to (ASSHTO 2001)
Number of lane = 4

## Slide 11: Horizontal Alignment
What is Horizontal Alignment?
Figure 6 - Horizontal curves road (al-madina)

## Slide 12: Horizontal Alignment Example of horizontal curve no. 3 (12+534.75)
12 + 534.75
Figure 7 - Horizontal curves Location (Google Earth pro)

## Slide 13
1-Mid ordinate:
2-Central Angle:
3-Degree of Curvature:
4-Length of Curvature:
5-Chord length:
6-External distance:
E = 15.07 m
7-Tangent length:
Station | Degree (Ɵ) | X (m) | Y (m) | L (m)
12+534.75 | 0 | 0 | 0 | 0
12+584.75 | 1.075 | 15.01 | 0.141 | 50
12+634.75 | 2.15 | 30.01 | 0.563 | 100
12+684.75 | 3.225 | 45.01 | 1.267 | 150
12+734.75 | 4.3 | 59.98 | 2.252 | 200
12+796.83 | 5.63 | 78.48 | 3.859 | 262.08
Table 6 - Points of Horizontal Curve no. 3
8-Points of curve:
Required stopping sight distance
<
Horizontal Alignment Example of horizontal curve no. 3 (12+534.75)

## Slide 14
Figure 8 - Details of horizontal curve no.3
Horizontal Alignment Example of horizontal curve no. 3 (12+534.75)

## Slide 15: Horizontal Alignment Example of horizontal curve no. 3 (12+534.75)
Figure 9 - Realistic simulation of horizontal curve no.3

## Slide 16: Results
There are five horizontal curves the following table shows summary of the horizontal curves' calculation.
Station PC | 2+600 | 7+627.80 | 12+543.75 | 18+467.34 | 23+041.75
R | 800 | 700 | 800 | 1000 | 900
M (m) | 9.75 | 11.13 | 10.74 | 10.2 | 11.32
 | 17.91 | 20.46 | 18.78 | 16.38 | 18.19
D (m) | 2.15 | 2.45 | 2.15 | 1.72 | 1.91
L (m) | 250 | 249.96 | 262.08 | 285.74 | 285.58
C (m) | 249.05 | 248.64 | 261.05 | 284.91 | 284.53
E (m) | 9.871 | 11.308 | 15.07 | 10.3 | 11.46
T (m) | 126.01 | 126.32 | 132.3 | 143.92 | 144.07
Station PC | 2+600 | 7+627.80 | 12+543.75 | 18+467.34 | 23+041.75
R | 800 | 700 | 800 | 1000 | 900
M (m) | 9.75 | 11.13 | 10.74 | 10.2 | 11.32
 | 17.91 | 20.46 | 18.78 | 16.38 | 18.19
D (m) | 2.15 | 2.45 | 2.15 | 1.72 | 1.91
L (m) | 250 | 249.96 | 262.08 | 285.74 | 285.58
C (m) | 249.05 | 248.64 | 261.05 | 284.91 | 284.53
E (m) | 9.871 | 11.308 | 15.07 | 10.3 | 11.46
T (m) | 126.01 | 126.32 | 132.3 | 143.92 | 144.07
Table 7 - Summary of the horizontal curves.
Horizontal Alignment

## Slide 17: Vertical Alignment
What is Vertical Alignment ?
Figure 10 - Vertical curves road (Freelik).

## Slide 18: Vertical Alignment Example of vertical curve no.1 (1+830.48)
1 + 830.48
Figure 11 - Vertical curves Location (Google Earth pro)

## Slide 19: Vertical Alignment Example of vertical curve no.1 (1+830.48)
Point | Station | X | 
PVC | 1+755 | 0 | 41.40
1 | 1+770 | 15 | 41.22
2 | 1+785 | 30 | 41.08
3 | 1+800 | 45 | 40.96
4 | 1+815 | 60 | 40.88
5 | 1+830 | 75 | 40.82
6 | 1+845 | 90 | 40.80
7 | 1+860 | 105 | 40.80
8 | 1+875 | 120 | 40.84
9 | 1+890 | 135 | 40.90
PVT | 1+905 | 150 | 41.00
Point | Station | X | 
PVC | 1+755 | 0 | 41.40
1 | 1+770 | 15 | 41.22
2 | 1+785 | 30 | 41.08
3 | 1+800 | 45 | 40.96
4 | 1+815 | 60 | 40.88
5 | 1+830 | 75 | 40.82
6 | 1+845 | 90 | 40.80
7 | 1+860 | 105 | 40.80
8 | 1+875 | 120 | 40.84
9 | 1+890 | 135 | 40.90
PVT | 1+905 | 150 | 41.00
1-Required stopping sight distance:
m <
2-Length:
3-Stations of PVC and PVT:
Table 8 - Elevations of the points along the vertical curve no. 1
4-Elevations of the points along the curve:

## Slide 20: Vertical Alignment Example of vertical curve no.1 (1+830.48)
Figure 12- Details of Vertical curve no.1

## Slide 21: Results
There are six vertical curves the following table shows summary of the vertical curves' calculation.
Vertical Alignment
Curve No. |  | 1 | 2 | 3 | 4 | 5 | 6
Classification |  | Sag (Type III) | Crest (Type I) | Sag (Type III) | Crest (Type II) | Crest (Type II) | Sag (Type III)
Length (m) |  | 150 | 150 | 70 | 100 | 100 | 100
Station (m) | PVC | 1+755.5 | 2+820 | 6+585 | 10+270 | 14+505 | 21+725
 | PVI | 1+830.5 | 2+895 | 6+620 | 10+320 | 14+555 | 21+775
 | PVT | 1+905.5 | 2+970 | 6+655 | 10+370 | 14+605 | 21+825
Elevation (m) | PVC | 41.40 | 47.71 | 20.80 | 24.59 | 23.45 | 2.35
 | PVI | 40.44 | 48.27 | 20.54 | 24.64 | 23.53 | 2.20
 | PVT | 41.00 | 47.72 | 20.58 | 24.63 | 23.38 | 2.31
Table 9 - Vertical curves summary

## Slide 22: Soil Investigation
The aim in this investigation is to calculate two values:
1-Californian Bearing Ratio (CBR)
2-Resilient Modulus ()
The samples were taken from three different locations of the project area at:
station 2+645 , station 18+645, and station 24+530

## Slide 23: Soil Investigation
Number of samples | Sample #1 | Sample #2 | Sample #3
Classification | Silty–sand (SM) | Poorly graded sand with silt (SP-SM) | Sandy silt of low plasticity (ML)
(mm) | 0.3 | 0.7 | 0.09
CBR | 18.25 | 24.72 | 11.86
(psi) | 16391 | 19904 | 12439
Station | 2+645 | 18+645 | 24+530
Number of samples | Sample #1 | Sample #2 | Sample #3
Classification | Silty–sand (SM) | Poorly graded sand with silt (SP-SM) | Sandy silt of low plasticity (ML)
 | 0.3 | 0.7 | 0.09
CBR | 18.25 | 24.72 | 11.86
 | 16391 | 19904 | 12439
Station | 2+645 | 18+645 | 24+530
Table 10 – Soil investigation summary
Notes: Where Diameter at 60% passing from the Grain Size Distribution – mm
Where D_60: Diameter at 60% passing from the Grain Size Distribution – mm

## Slide 24
Soil Profile
Figure 13 - Soil Profile at Project site
Layers specifications for intersection of the road with the railway located at station 1+270

## Slide 25: Pavement Design
Surface Course.
Base Course.
Subbase Course.
Figure 14 – Pavement layers
Source: Transportation Engineering Slides, Dr. M. Khasawneh, Ph.D

## Slide 26: Summary Table
Table 11 – Summary values of pavement design
Pavement Design

## Slide 27: Pavement Design Design 1st
Asphalt Course:
D1 = 10 in
Base Course:
D2 = 15 in
Sub – Base :
D3 = 12 in

## Slide 28
Asphalt Course:
D1 = 6 in
Base Course:
D2 = 7 in
Sub – Base :
D3 = 9 in
Pavement Design Design 2nd

## Slide 29
Figure 15 - Final pavement design
Pavement Design
Design 2

## Slide 30: Drainage system
Characteristics of natural basins
Mean intensity
Hydraulic Design

## Slide 31
Drainage System
Section | Area (km2) | Highest Elevation (m) | Lowest Elevation (m) | Slop (%)
17+200 – 19+890 | 33.5 | 7 | 1 | 0.3
Table 12 - Basins Characteristics
Characteristics of natural basins
Figure 16 - Natural basins location (Google Erath Pro)
The design period (50) years.

## Slide 32
Duration (hours) | Return period T (Years) |  |  |  | 
 | 2 | 5 | 10 | 50 | 100
 | Mean intensity (mm/h) |  |  |  | 
1 | 45.16 | 64.2 | 76.8 | 104.5 | 116.2
2 | 60.9 | 89.2 | 107.8 | 148.8 | 166.2
6 | 77.34 | 128.1 | 161.8 | 235.8 | 267.2
12 | 85.32 | 143.9 | 182.8 | 268.2 | 304.3
24 | 93.9 | 154.5 | 194.7 | 283 | 320.3
Table 13 - Mean intensity
Mean intensity () calculation:
Drainage System
: mean of the rainfall data.
S: Standard deviation of the rainfall data.
: Frequency factor.
C: Runoff coefficient
I: Intensity/Rainfall rate, mm/h.
A: Area of drainage basin, .
Inflow calculation, Q:
Q = 0.278 CIA
Q = 0.278 × 0.75 × 104.5 × 33.5
Q = 730 .

## Slide 33
Figure 17 - Gutter flow cross section definition of terms (HDM)
Hydraulic Design
d = 16 × 0.02 = 0.32 m = 32 cm
s = 0.89 % → let s = 1%
Drainage System
W = (20 - 4)= 16 m
Curb depth:
Calculation the slope of maximum
gutter flow Q by:
K: constant = 0.38 .
z: reciprocal of the cross-transverse slop of the gutter. n: roughness coefficient of surface = 0.016.
s: slop of the gutter.
Transvers slope.
y: water depth in the gutter at the curb.
Transvers slope is 2%
Ponded width of flow:
T >

## Slide 34
Figure 18 - Cross-section of road in cut/fill
Drainage System

## Slide 35
Figure 19 - Cross-section of super elevation
Drainage System

## Slide 36: Intersection Design
Selected Interchange
Interchange's locations
Ramps Design
Summary

## Slide 37
Figure 20 - Three legs interchanges types (AASHTO 2001)
Selected Interchange
Freeway-freeway intersection:
Interchange.
Locations of interchanges at start and end points:
Three legs: (Trumpet-B)
Semidirect directions:
Designed Road Heading Abqaiq City.
Designed Road Heading Half-moon.
Intersection Design

## Slide 38: Intersection Design
Intersection Station | Interchange Location | Interchange classification | Type
0+000 | Al Dharan – Abqaiq Rd. | Three legs | Trumpet - B
26+275 | Al Khobar – Salwa Rd. | Three legs | Trumpet - B
Table 14 - The required interchanges
Figure 21 - Interchanges Locations (Google Earth Pro)
Interchange's locations
0 + 000
26 + 275

## Slide 39
Ramp Type | Lanes No. | Speed Design (km/h) | Radius (m) | La, Exist (m) | La, Enter (m)
Loop | 2 | 70 | 175 | 230 | ----
Outer Connection #1 | 2 | 90 | 275 | 210 | 245
Outer Connection #2 | 2 | 90 | 275 | 210 | 245
Semidirect | 2 | 90 | 275 | ----- | 245
Table 15 - Summary of the interchange design
Summary
Intersection Design

## Slide 40
Figure 22 - Realistic simulation of final interchange
Summary
Intersection Design

## Slide 41: Bridge Design Sub – Project
Layout
Girders
Pier Cap
Pier
Foundation
Loads

## Slide 42
Geometric description:
Supporting conditions: Simply Supported Span
Span length: ~ 24.4 m
Lane width: ~ 3.35 m
Cross section width, including
shoulders: ~ 15.2 m
Layout
Figure 23 - Realistic simulation of the bridge
Bridge Design
Pier Cap
Girders
Pier
Foundation

## Slide 43
Layout
Figure 24 - sideview of the bridge
Bridge Design

## Slide 44: Bridge Design
Load calculations: Dead load
Asphalt load
Slab (light weight) =
Total superimposed dead load =
Load calculations: Live load
Number of trucks =
Load per truck
Total truck load
Equivalent distributed truck load =
Total superimposed live load =
Loads
Figure 25 - Superimposed live load (AASHTO 2001)

## Slide 45: Bridge Design
Figure 26 - PCI section selection (PCI)
Girders
Section: 12DT34

## Slide 46
Pier Cap
Max M+ = 611 KN.m
Max M- = 825 KN.m
Max V = 550 KN
R = 1100 KN
Figure 27 - Cross section of the pier cap
Bridge Design

## Slide 47
Pier design
Max M = 266 KN.m
Max axial force = 460 KN.m
The reinforcement percentage , ρ = 0.01
Gross area ,
Area of steel , = 5000
Figure 28 - Cross section of the pier
Bridge Design

## Slide 48
Foundation
Depth , = 1.00 m
Width , B = 2.20 m
Thickness , h = 0.4 m
Ultimate moment , = 55.6 KN.m
Area of steel , = 720 /
Figure 29 - Reinforcement detailing of the foundation
Bridge Design

## Slide 49: Cost Estimation.
Cost Estimation Criteria
Cost Estimation Agenda

## Slide 50: Cost Estimation.
Cost Estimation Criteria
1.Cut and fill quantities.
2. Leveling of ground.
3. Material price.
4. Equipment work time.
5. Labor's price.
6. Management cost.
7. External expenses.

## Slide 51: Cost Estimation.
Cost Estimation Agenda
Highway
Total cost of the Highway = 81,951,552 SAR
Bridge
Total cost of the Bridge = 561,040 SAR
Operation
Cost of the Operation = 8,251,259 SAR

## Slide 52
Ministry of Transportation General Administration of Roads and Transportation in the Eastern Region | 
Project Title: Abqaiq – Half-moon Highway Design with Reinforced Concrete Bridge Design Section. | 
Contractor & Consulting: Group one: Alhajji, Albasha, Alshammari, Alkhalifah. Co | 
Date of signing the contract 2020/12/27 | The date the contractor was notified of the contract 2020/10/08
Project end date (initial) 2022/05/10 | The date of the start of the project implementation 2021/01/01
Advisor : Dr. Mohammed Ali Coordinator: Dr. Andi Asiz | Duration of contract extension After the expiry date of the contract
Total cost : 90,763,852 SAR | 
Table 16 – Construction

## Slide 53: Summary & Conclusions.
Complexity
Final Modeling of the project.

## Slide 54: References

## Slide 55: Thank you for listening
ASSE 4311
Learning Outcome Assessment III CE
Final Presentation
Group 1
(We are happy to answer your recommendations and questions)