## Slide 1
Design of 30-Storey Tower Using RC & CLT in Dammam
Advisors:
Engr. Danish Ahmed
Dr. Tahar Ayadat
Coordinator:
Dr. Andi Asiz
Learning Outcome Assessment III
Final
1
  Student Names & ID’s:
1- Abdel Aziz Albobali, 201400523
2- Ammar Alshaki, 201102686
3- Yasser Bekheit, 201502739
4- Naif Bin Mahfouz, 201401393

## Slide 2
2
Outline
Project Objectives
Project Scope
Project Description
Codes and Design Specifications
Project Constraints
Structural Design of the Building
ETABS Modelling
Geotechnical and Foundation System Design
Cost Estimation
Summary

## Slide 3
3
Project Objectives
Design and analysis of 30-Storey building (+ 5 Basements ), including:
Selection of codes and design specifications
Performing the analysis between two different floor systems.
Project constraints
Structural design of the building, and checking the design using ETABS
Geotechnical design of the foundation system
Comparing the two structure system
Assure sufficient parking lot for building purposes

## Slide 4
Codes and Design Specifications
4
Saudi Building Code structural requirements (SBC):
Loading and Forces (SBC 301),
Concrete Structures (SBC 304),
Soil and Foundations (SBC 303),
Steel Structures (SBC 306).

## Slide 5
Project Scope
Chapter | Description
Project Description | Description of the of the original and modified layout
Project Constraints and Structural Design | Required codes and the detailed design of the structure
Preliminary Design | The design of the ( slab , beam, and column ) sections
Steel Reinforcement | Choose suitable size steel bars for reinforcement
Used Software | Using ETABS and AutoCAD modeling
Geotechnical Design and Foundation System | Design applicable foundation system according to the geotechnical properties
Comparing the two Systems | Comparison between CLT and RC system
Cost Estimation | Provide the cost estimation of each material we used
4

## Slide 6
5
Project Constraints
Constraints |  | Solutions
Geotechnical | High level of water table (0.45 m - 1.3 m) | Consider temporary dewatering and permanent drainage system
 | Sabkha Soil (Difficult Soil) | Removal of the contaminated Sabkha soil
 | Foundation Design | Using the mat with pile due to the huge settlement
Material | High Sulfate content in soil | Using type V cement
 | High Chloride content in soil | Application on structural members epoxy or bitumen coating
Environmental | Contaminated “Sabkha” soil | Disposal of excavated contaminated soil and water
Structural | Deflection limits and stability | Consider all possible load combination cases
 | Load combination cases | 
Cost | All previous constrains | Applying standards and codes to minimize the overall cost

## Slide 7
6
Project Description (Original/Actual)
Designed by (AFM) consultants
15 floors
80 m in length
42 m in width
57.3 m in height
Elevation per floor 4 m
SIDE ELEVATION

## Slide 8
7
Project Description (Edited/Modified)
30 floors (+5 Basements)
80 m in length
42 m in width
136 m in height
Elevation:
Basement: 3 m, Ground floor: 5 m, All other floors: 4 m
3D
GRIDLINE

## Slide 9
RESIDENTIAL
Floor 18 to 30 (13 floors)
RECREATIONAL
Floor 15 to 17 (3 floors)
COMMERCIAL
Floor 1 to 14 (14 floors)
PARKING
Basement 5 + Ground floor (6 floors)
8
Project Description

## Slide 10
9
Project Description (Location)
Sihat
Round-about
Sihat
Round-about

## Slide 11
Structural Design of the building
12
Preliminary:
Load combinations formulae used:
ETABS Modeling
    Slab
    Beams
Columns
    Shear Walls

## Slide 12
15
Structural Design

## Slide 13
Slab
*
*
Structural Design
13

## Slide 15
Beams
*
* Cross section of beam:
14
Structural Design

## Slide 17
Gross area for columns and shear wall
16
Structural Design
* Cross section of columns:

## Slide 20
17
Extended Three Dimensional Analysis
of Building Systems;
Gridlines
3D view of the structure
Members Analysis
Wind – Seismic loads
Deflection Mapping
Structural Design
  ETABS © Modeling and Analysis

## Slide 21
18
Structural Design
  ETABS © Modelling and Analysis

## Slide 22
19
Structural Design
  ETABS © Modelling and Analysis

## Slide 23
20
Geotechnical Design of Foundation System
  Soil Profile
  Chemical Analysis

## Slide 24
Soil Profile
Boreholes | Soil Description | Range of SPT “N” values
BH-1 to BH-5 | Layer: 1 ( 0.0m - 2.50m ) brownish to dark gray, very loose to loose,silty sand | 4 – 10 ( loose )
 | Layer: 2 (2.50m – 9.00m) dark gray, yellowish to grayish ,very soft , sandy lean clay ( sabkha) | 1 – 13 ( loose)
 | Layer:3 ( 9.00m – 12.00m) grayish to brownish , medium dense, poorly graded | 14 – 23 ( medium )
 | Layer: 4 (12.00m -15.00m) gray to brownish, hard, sandy lean clay medium dense to dense | 17 – 47 (medium to dense )
 | Layer: 5 (15.00m - 25.00m) gray to brownish , hard , sandy lean clay | 21 - > 50 (medium dense – dense very dense )
 | Layer: 6 (25.00m - 30.50m) gray to brownish , hard , sandy lean clay | 47 - > 100 ( very dense )
10

## Slide 25
Soil Profile
10

## Slide 26
Chemical Analysis
Chemical analysis (Sulfate & Chloride)
Type of materials | Type of test | Chemical con. | 
 |  | Sulfate(%) | Chloride(%)
Soil | Acid Soluble | 0.195-0.424 | 1.277-2.528
11

## Slide 27
20
Obtained Soil Profile and Chemical Analysis
High level of water table ​ (0.45 m - 1.3 m)​ | Consider temporary dewatering and permanent drainage system​
Sabkha Soil (Difficult Soil)​ | Removal of the contaminated Sabkha soil​
Foundation Design ​ | Using the mat with pile due to the huge settlement ​

## Slide 28
20
Geotechnical Design of Foundation System
  Piled Raft Foundation

## Slide 29
20
Geotechnical Design of Foundation System
  Piled Raft Foundation

## Slide 30
Required Foundation System
(System #3: Piled Mat Foundation )
http://www.abuildersengineer.com/2012/12/piled-foundations-typical-examples.html
21

## Slide 31
22
Cost Estimation
Floor | Area m2 | Unit price SAR/m2 | Cost
Basement | 3314.8 × 5 | TBD | TBD
Ground | 2198.54 × 1 | TBD | TBD
Floors | 1424.44 × 29 | TBD | TBD
Total | 60081.3 | TBD | TBD

## Slide 32
References
25
Saudi Building Code (SBC)
American Concrete Institute. ACI. (2014). Building code requirements for structural concrete (ACI 318-14).
Soil Profile and Chemical Analysis
CSI© ETABS© 2016 Ultimate; version 16.2.0
Autodesk© AutoCAD© 2019: Educational Version.
Lecture notes Geotechnical , foundation , concrete ,structural and environmental

## Slide 33
26
Thank You
Any Questions ?