## Slide 1
ASSE 4311: Learning Outcome Assessment III Final Presentation
Structural & Geotechnical Design of a Multistory Building using RCC & CLT
Coordinator’s name
Dr. Andi Asiz
Engr. Danish Ahmed
Supervisor’s name
Submitted By Group 5
Mohammed Abdi 201503119
Ali Al Khatim 201200808
Nasser Banihameem 201201710
Ahmed El- Ghoneimy 201601198
Examiner's name
Dr. Tahar Ayadat
Examiner's name
Dr. Mohammad Khasawneh

## Slide 2
OBJECTIVES
OUTLINES
PROJECT DESCRIPTION
STRUCTRAL DESIGN
METHODOLOGY
GEOTECHNICAL DESIGN
PROJECT CONSTRAINTS
PROJECT SUMMARY
COMPARISON BETWEEN RCC &CLT

## Slide 3
3

## Slide 4
The location of the building is on Al Aziziyah, Khobar, Saudi Arabia
(Google Map 2021) [1]
Project Location

## Slide 5
Purpose:
Residential & Commercial building
Number of Storeys:
13 Floor
Area of the Building:
1330 m2
Height of Building:
48 m
Height of floor:
Parking 3.5 m
Ground floor 4.25 m
Each floor 3.60 m
Project Description
Elevation View of the project [4]

## Slide 6
Structure | Function
Two Basement Floor | Parking
Ground Floor | Health Club
First Floor | Commercial
Second Story to the Roof | Residential
Floor Planning & Utilization
Table (1):Floor Plan

## Slide 7
Original layout (MDCEO, 2021) [4]
Original Layout

## Slide 8
Basement layout of the project [4]
Modified Layout

## Slide 9
Layout of the replicated floors of the project [4]
Replicated Floor Layout

## Slide 10
1
Methodology
3
Concrete Structural
Element Design
2
5
ETABS Modeling
4
CLT Structural
Element Design
Structural Design
Structural Loads

## Slide 11
Layout Drawing
Loads &load combinations
ETABS
Saudi Building Code
Structural Elements
Constraints
Methodology
Methodology
11

## Slide 12
Types of Loads acting on the Structure:
1- Dead loads
2- Live loads
3-Wind loads (x,y)
4- Earthquake (x,y)
5-Load combinations
Loads acting on the Structure
Load Directions [8]

## Slide 13
Live Loads & Dead Loads acting on the structure
Structure | Dead Load | Live Load
Parking | 2 | 10
Health club | 2 | 4
Commercial | 2 | 5
Residential | 2 | 2
Structure |  | 
Parking | 2 | 10
Health club | 2 | 4
Commercial | 2 | 5
Residential | 2 | 2
Table (2): Dead Loads & Live Loads
Finishing Dead Loads Table | Load
Total | 2.00
References Saudi Building Code [6] | 
Finishing Dead Loads Table | Load
Total | 
References Saudi Building Code [6] | 

## Slide 14
Wind Loads
Wind Loads acting on the structure:
All Parameters have been taking from SBC[6] for Eastern province region
Wind speed = 94.448 mph, =152 Km/h
Exposure type = C
Gust Factor =0.85
Directionality Factor, Kd = 0.85
Retrieved from ETABS

## Slide 15
Seismic Loads
Seismic Loads EQ (X,Y) :
All Parameters been taking from SBC [6]
for Eastern province region
Ss=0.33
S1=0.11
Transition Period=8 sec
site type = D
R=6.5
Omega=3
Cd=5.5
I=1.25
Retrieved from ETABS

## Slide 16
Loads Combinations
Type | Combination
Dead Load and Live Load | 1.2(DL) + 1.6(LL) (Design and calculation use)
DL and Wx | 0.9(DL) + 1.6 (WLX)
DL and Wy | 0.9(DL) + 1.6(WLy)
DL and Eqx | 1(DL) + 1(Eqx)
DL and Eqy | 1(DL) + 1(Eqy)
References ASCE Code [3] | 
Table (3):Load Combinations

## Slide 17
RCC Structural Elements
Slab Design and Reinforcement
Beams Design and Reinforcement
Column Design and Reinforcement
Shear Walls Design and Reinforcement

## Slide 18
RCC Slab Design
RCC Slab Design location :
Slab 2
Slab 1
Slab 3
Critical Slab

## Slide 19
RCC Slab Calculation
4.8 m
3.8 m
Slab 2
Slab 1
Slab 3
3.8 m
4 m
5 m
5 m

## Slide 20
Critical Slab 3
4 m
5 m
RCC Critical Slab
Critical Slab
s
S

## Slide 21
RCC Critical Slab Reinforcement
Two Way Slab Reinforcement [3]
Cut Cross-section of the Slab Reinforcement

## Slide 22
4m
5m
2.4 m
Location [1] : 5m
Location [2] : 4m
Location [3] : 2.4m
Beams Locations
RCC Beam Design location:
RCC Beam Design

## Slide 23
RCC Critical Beam Calculation
RCC Beam Design (Critical Beam 5m)
Location [1] : 5m
5m
Ast
d=250mm
b=170 mm
h=320mm
Ratio
Cross section beam
Retrieved from ACI [2]
23

## Slide 24
RCC Critical Beam Reinforcement
Beam Dimensions (5m) cross-section(450mm x 260mm)
All data has been taking from ETABS
Area of steel top= 338 mm2
Area of steel bottom= 430 mm2
Beam Reinforcement Detail (retrieved from ETABS)
Provide 10@ 100mm stirrups c/c
Beam Stirrup (retrieved from ETABS)[3]

## Slide 25
A1
A2
A3
A4
A5
A6
A7
B7
B6
B5
B4
B3
B2
B1
C1
C2
C3
C4
C5
C6
C7
D7
D6
D5
D4
D2
D1
E1
E2
E4
E5
E6
E7
F7
F6
F5
F3
F2
F1
G1
G2
G5
G6
G7
H7
H6
H5
H4
H2
H1
I1
I2
I3
I4
I5
I6
I7
J7
J6
J5
J4
J3
J2
J1
K1
K2
K3
K4
K5
K6
K7
RCC Columns Location
RCC Column Design

## Slide 26
RCC Column Design Calculation
=Axial load acting on the element (in kN or kips).
Safety factor for a rectangular element ≈ 0.65 (unitless)
Safety factor for a rectangular column ≈ 0.80 (unitless)
Compressive strength of the concrete (using 4000 psi)
ield strength of the concrete (using 60000 psi)
Gross area of the concrete element.
rea of steel required
Retrieved from ACI [2]
Column [8]

## Slide 27
RCC Types of Column
Exterior
Column | Cross section (mm)
8th Story | 200x200 mm
5th Story | 220x220 mm
2nd Story | 250x250 mm
G Story | 280x280 mm
B1 Story | 300x300 mm
Column | Cross section (mm)
8th Story | 220x220 mm
5th Story | 230x230 mm
2nd Story | 300x300 mm
G Story | 320x320 mm
B1 Story | 380x380 mm
27
Corner
Table (5):Cross Sections
Table (4):Cross Sections

## Slide 28
RCC Types of Column
Column | Cross section (mm)
8th Story | 250x250 mm
5th Story | 300x300 mm
2nd Story | 380x380 mm
G Story | 420x420 mm
B1 Story | 480x480 mm
Column | Cross section (mm)
8th Story | 300x300 mm
5th Story | 350x350 mm
2nd Story | 400x400 mm
G Story | 430x430 mm
B1 Story | 500x500 mm
28
Interior
Center
Table (6):Cross Sections
Table (7):Cross Sections

## Slide 29
RCC Critical Column Reinforcement
Column 480mm x 480mm
(All data has been taking from ETABS) ,( Area of steel 4236 mm2 ),( Using #22 dimeter), (Provide 12#22 )
Column Reinforcement Detail (retrieved from ETABS)
Column Stirrup (retrieved from ETABS)[3]
12 ties @ 300 mm c/c

## Slide 30
Shear Wall Design
Shear wall
6.3 m
2.4 m
6 in
Retrieved from ACI [2]
RCC Shear wall Design

## Slide 31
Length 6300 mm Thickness 160mm
All data has been taking from ETABS
Area of steel 7346 mm2
Using #29 dimeter:
Provide 12#29
RCC Critical Shear wall Reinforcement
Critical Shear wall
Shear wall Reinforcement Detail (retrieved from ETABS)

## Slide 32
Slab Design
Column Design
CLT Structural Elements
CLT

## Slide 33
Mechanical properties of CLT slab
Mechanical properties of CLT slab | Orthotropic
Directional Property | Orthotropic
Density(kg/m3) | 400
Elastic Modulus (GPa) | E1=9,E2=4.5,G12=0.5
Poisson’s Ratio | V1=0.3
Strength (MPa) | Ft-1=20,ft-2=15,fc-1=30,fc-2=25,fshear=5
Notation: E = modulus of elasticity; G = modulus of rigidity; 1 = CLT major direction; 2 = CLT minor direction; t = tension; c = compression | 
Table (8):Mechanical properties [9]

## Slide 34
CLT Slab Design
150 mm
300 mm
CLT Slab Deflection with 150 mm
CLT Slab Deflection with 300 mm

## Slide 35
CLT Columns Design Calculation
=Axial load acting on the element (in kN or kips).
Safety factor for a rectangular element ≈ 0.65 (unitless)
Safety factor for a rectangular column ≈ 0.80 (unitless)
Compressive strength of the concrete (using 4000 psi)
ield strength of the concrete (using 60000 psi)
Gross area of the concrete element.
rea of steel required
RCC column with CLT Slab
Retrieved from ACI [2]

## Slide 36
CLT Types of Column
Exterior
Column | Cross section (mm)
8th Story | 200x200 mm
5th Story | 210x210 mm
2nd Story | 220x220 mm
G Story | 230x230 mm
B1 Story | 250x250 mm
Column | Cross section (mm)
8th Story | 200x200 mm
5th Story | 220x220 mm
2nd Story | 250x250 mm
G Story | 260x260 mm
B1 Story | 300x300 mm
36
Corner
Table (10):Cross Sections
Table (9):Cross Sections

## Slide 37
CLT Types of Column
Column | Cross section (mm)
8th Story | 200x200 mm
5th Story | 250x250 mm
2nd Story | 300x300 mm
G Story | 350x350 mm
B1 Story | 400x400 mm
Column | Cross section (mm)
8th Story | 200x200 mm
5th Story | 250x250 mm
2nd Story | 300x300 mm
G Story | 350x350 mm
B1 Story | 400x400 mm
37
Interior
Center
Table (11):Cross Sections
Table (12):Cross Sections

## Slide 38
CLT Critical Column Reinforcement
Column 400mm x 400mm
(All data has been taking from ETABS) ,( Area of steel 1600 mm2 ),( Using #13 dimeter), (Provide 12#13 )
Column Reinforcement Detail (retrieved from ETABS)
Column Stirrup (retrieved from ETABS) [3]
12 ties @ 200 mm c/c

## Slide 39
CLT Critical Beam Reinforcement
Beam Dimensions (5m) cross-section(450mm x 260mm)
All data has been taking from ETABS
Area of steel top= 338 mm2
Area of steel bottom= 338 mm2
Beam Reinforcement Detail (retrieved from ETABS)
Provide 10@ 100mm stirrups c/c
Beam Stirrup (retrieved from ETABS)[3]

## Slide 40
ETABS Modeling
ETABS Modeling

## Slide 41
ETABS Modeling
Elevation View
Plane Floor View
3D View

## Slide 42
RCC Slabs Deflection
RCC Slab Deflection (Dead Load + Live Load)
Slab Deflection after applying the highest load
3.6mm < 25mm
ACI (Passed)

## Slide 43
CLT Structure Modeling
CLT Slab Deflection (Dead Load + Live Load)
Slab Deflection after applying the highest load
2.28mm < 25mm
ACI (Passed)

## Slide 44
Elements Frame Check
RCC All Frames Passed
CLT All Frames Passed

## Slide 45
Displacement for RCC
Maximum story displacement for (Seismic load)
Maximum story displacement for (Wind load)

## Slide 46
Displacement for CLT
Maximum story displacement for (Seismic load)
Maximum story displacement for (Wind load)

## Slide 47
Geotechnical Design
Analysis of Different Foundation Design:
Geotechnical design:
Isolated Foundation
Raft (Mat Foundation)
Pile Foundation
Raft with Pile
Soil Profile
Soil Analysis
Soil Layers (MDCEO, 2021) [4]

## Slide 48
Soil Profile & Analysis
Modified Soil Layers After excavating (MDCEO, 2021) [4]
Temporary Dewatering
Permanent Dewatering
Well Point System
French Drainage System

## Slide 49
Alternative Foundation Design
Isolated Foundation:
Q=
7m
16m
2m
Isolated foundation Design [4]
The net allowable soil bearing capacity (kN/m2) |  | Bearing Capacity of the Soil (kN/m2)
 | < | (Not ok)
The net allowable soil bearing capacity (kN/m2) |  | Bearing Capacity of the Soil (kN/m2)
 | < | 
Table (13):Bearing Capacity

## Slide 50
RCC Raft Foundation:
The soil pressure under each column:
The bearing capacity of the soil:
Critical Soil Point Pressure (kPa) |  | The bearing capacity of the soil(kPa)
 | < | 
Critical Soil Point Pressure (kPa) |  | The bearing capacity of the soil(kPa)
 | < | 
Raft foundation Design [4]
Alternative Foundation Design
Table (14):Reinforcement Detail Selection

## Slide 51
Pile with Raft Foundation:
Pile foundation with raft Design [4]
D= 30 cm
L= 23m
No. of Piles=77
Alternative Foundation Design

## Slide 52
RCC Raft Foundation Reinforcement
Soil Reaction =
Critical Strips (retrieved from ETABS)

## Slide 53
Raft RCC Foundation Reinforcement
Critical Strip 39 m

## Slide 54
Raft RCC Foundation Reinforcement
Spacing | Diameter(mm) | Spacing (mm) c/c | As provided (mm2)
Top | 29 | 80 | mm2
Bottom | 29 | 80 | mm2
Spacing | Diameter(mm) | Spacing (mm) c/c | As provided (mm2)
Top | 29 | 80 | 
Bottom | 29 | 80 | 
Table (15):Reinforcement Detail Selection
Foundation Reinforcements
20#29@80mm c/c
20#29@80mm c/c
20#29@80mm c/c
20#29@80mm c/c

## Slide 55
CLT Raft Foundation:
The soil pressure under each column:
The bearing capacity of the soil:
Critical Soil Point Pressure (kPa) |  | The bearing capacity of the soil(kPa)
 | < | 
Critical Soil Point Pressure (kPa) |  | The bearing capacity of the soil(kPa)
 | < | 
Raft foundation Design [4]
Alternative Foundation Design
Table (16):Reinforcement Detail Selection

## Slide 56
CLT Raft Foundation Reinforcement
Soil Reaction =
Critical Strips (retrieved from ETABS)

## Slide 57
Raft CLT Foundation Reinforcement
Critical Strip 39 m

## Slide 58
Raft CLT Foundation Reinforcement
Table (17):Reinforcement Detail Selection
Spacing | Diameter(mm) | Spacing (mm) c/c | As provided (mm2)
Top | 25 | 90 | mm2
Bottom | 25 | 90 | mm2
Spacing | Diameter(mm) | Spacing (mm) c/c | As provided (mm2)
Top | 25 | 90 | 
Bottom | 25 | 90 | 
Foundation Reinforcements Details
15#25@90mm c/c
15#25@90mm c/c
15#25@90mm c/c
15#25@90mm c/c

## Slide 59
RCC Cost Estimation
Cost Estimation of RCC Structure |  |  |  |  |  | 
No. | Materials | Volume (m3) | Unit Price (SR/m3) | Unit Price(SR) |  | Cost (SR)
1 | Concrete | 4635.4 | 210 | -------------- |  | 973,434
2 | Reinforcement | (4635.4 * 160)/1000 Kg/m3 | ----------------- | 742 ton* 2600 |  | 1,929,200
3 | Finishing | 60%of the Total cost | -------------- | -------------- |  | 1,741,580
Prices of the material was provided by MADCO for contracting company, 2021
Total Project Cost = SAR4,644,214
Table (18):RCC Cost Estimation

## Slide 60
CLT Cost Estimation
Cost Estimation of CLT Structure |  |  |  |  |  | 
No. | Materials | Volume (m3) | Unit Price (SR/m3) | Unit Price(SR) |  | Cost (SR)
1 | CLT Slab | 4352.4 | 1200 | -------------- |  | 5,222,880
2 | Concrete | 1071 | 210 | -------------- |  | 224,910
3 | Reinforcement | (1071 * 160)/1000 Kg/m3 | ----------------- | 171 ton* 2600 |  | 444,600
4 | Finishing | 60% of the Total cost | -------------- | -------------- |  | 3,535,434
Prices were taking from PMU library (senior project, 2018)
Total Project Cost = SAR 9,427,824
Table (19):CLT Cost Estimation

## Slide 61
Project Constraints
Table (20):Project Constraints
Constraints |  | Solutions
Structural (sizes of the beams & columns) |  | Increasing Cross-Sections of Beam Increasing Cross-Sections of columns
Geotechnical |  | Applying Temporary Dewatering & Permanent Dewatering system
Material (CLT) |  | More research and used computer software such us ETABS
Cost |  | Using PMU Library for previous senior design project for CLT cost
Environmental |  | Follow the PME's environmental plan to protect Saudi's health and natural resources

## Slide 62
Project Complexity
Complexity | Uniqueness
Soil Treatment | Distinguish location
Location | Spectacular scenery
CLT option | First of its own
Special arrangement | CLT option
-------------------- | PMUs Graduating Students
Table (21):Project complexity

## Slide 63
Comparison Between RCC & CLT
 | RCC | CLT
Cost | Economically | Costly
Durability | More Durable | less Durable
Construction | Longer Period of time | Shorter Period of time
Environmentally | Environmentally Harmful | Environmentally Friendly
Strengths | Strong | Strong
Safety | Fulfilled all Safety Requirements | Fulfilled all Safety Requirements
Table (22):Comparison

## Slide 64
Project Summary & Conclusion
Aim of This Project
Design of a Multistory Building
Software Program Analysis
Comprehensive Study of The Foundation System
Comprehensive Cost Estimation
Final Thoughts

## Slide 65
Location Google map, Saudi Arabia,2021.
American Concrete Institute. ACI. (2014). Building code requirements for structural concrete (ACI 318-14). Farmington Hills, Michigan.
3. PMU library senior design project, design of 60 story RCC&CLT connected twin towers in Al-Khobar, 2018
Modern Designing Consulting Engineering Office (MDCEO),Saudi Arabia,2021
Cross-laminated Timber: Design and Performance, Exova BM TRADA, 2017 - Engineered wood construction - 153 pages.
Saudi Building Code National Committee (SBCNC), 2007.
CSI ETABS Program. (n.d.). Retrieved from Computer and Structures. (2016).
Bhatt and MacGinley, T. (n.d.). (2017) Reinforced concrete design to Eurocodes.
Asiz, A., Smith, I. (2009), Demands Placed on Steel Frameworks of Tall Buildings Having Reinforced Concrete or Massive Wood Horizontal Slabs, Structural Engineering International, Vol. 19, No. 4, 395-403 (9).
REFERENCES
Structural Design of a Multistory Building using RCC & CLT

## Slide 66
Thank You