## Slide 1: Final Presentation Structural & Geotechnical Design of a Hotel in the Area of Half Moon Bay
Abdalla Shalata 201200594
Mohammed Al-Shiha 201400215
Ali Abualhatal 201202539
Fall 2016 ASSE 4311: Learning Outcome Assessment III/Civil Engineering 18/1/2017
Advisors: Dr. Tahar Ayadat
Engr. Danish Ahmed

## Slide 2: Presentation Outline
1. Introduction
2. Project objectives
3. Project design
2.1 Calculation and analysis
2.2 Structural design
4. Foundation design
3.1 Geotechnical design
3.2 Foundation Systems
3.2.1 Shallow foundations
3.2.2 Deep foundation (Piles)
5. Conclusion

## Slide 3: 1- Introduction
Half-moon bay is a semi-lunar arch with several attractions: entertainment zones and amusement cities
It is a major recreational area for tourists, who throng the area on the weekends.
Construction of hotels in the area is still not receiving full consideration.

## Slide 4: 2- Project objectives
The main objectives of the project are to design a multistory hotel of irregular floor layout in the Half-Moon bay, which includes:
Structural design of the superstructure of the multistory hotel.
Geotechnical analysis and design of appropriate foundation systems of the hotel.

## Slide 7: Typical Floor Plan

## Slide 8: Typical Parking Plan

## Slide 9: 3- Project design
3.1 Calculation analysis:
3.1.1 Area Calculation
Name | Area in the plan (cm²) | Area in the field (m²)
S1 | 10.58 | 26.22
S2 | 11.67 | 28.29
S3 | 9.03 | 22.38
S4 | 14.4045 | 35.69
S5 | 23.9525 | 59.35
S6 | 10.4575 | 25.91
S7 | 11.12625 | 27.57
S8 | 10.63875 | 26.36

## Slide 10
3.1.2 Load Calculation (Saudi Building Code)
floor | pu (kN) | cumulative PU (kN) | Ag cm2 | column length cm
Roof | 1505 | 1505 | 1149.73262 | 
7 | 6329 | 7834 | 5984.72116 | 
6 | 708 | 8542 | 6525.59206 | 217.5197352
5 | 708 | 9250 | 7066.46295 | 
4 | 708 | 9958 | 7607.33384 | 
3 | 708 | 10666 | 8148.20474 | 271.6068245
2 | 708 | 11374 | 8689.07563 | 
1 | 708 | 12082 | 9229.94652 | 
G floor | 4203 | 16285 | 12440.7945 | 414.69315
-1 | 540 | 16825 | 12853.3231 | 
-2 | 540 | 17365 | 13265.8518 | 
-3 | 540 | 17905 | 13678.3804 | 455.9460148

## Slide 11: 3.2 Structural Design
The structural design of the hotel was performed using ETABS.
The hotel is composed of twelve floors or stories.
Each floor will cover an area of about 1870 m2
The maximum live load is taken to be 6.4 KN/m2.

## Slide 12: 3.2 Structural Design (continued)
Floor # | Calculated Dead load | Calculated Live load
Floor | Dead load (KN/m²) | Life load (KN/m²)
Swimming pool + GYM | 7.1175 | 5
Mechanical room (7) | 7 | 2.68
6 | 7.1175 | 2
5 | 7.1175 | 2
4 | 7.1175 | 2
3 | 7.1175 | 2
2 | 7.1175 | 2
1 | 7.1175 | 2
G | 7.1175 | 6.4
Parking (1) | 7 | 4.9
Parking (2) | 7 | 4.9
Parking (3) | 7 | 4.9

## Slide 13: 3.2 Structural Design (continued)
Steel bars reinforcement options for positive moment design
Bar # | Number of bars | Total area of bars (in2) | Cross sectional area of one bar (in2) | Bar-to-bar spacing (in)
5 | 6 | 1.86 | 0.31 | To be calculated
6 | 4 | 1.76 | 0.44 | To be calculated

## Slide 14: 3.2 Structural Design (continued)
Steel bars reinforcement options for negative moment design
Bar# | Number of bars | Total area of bars (in2) | Cross sectional area of one bar (in2) | Bar-to-bar spacing (in)
5 | 6 | 1.86 | 0.31 | 0.8944 (calculated in the positive moment design)
5 | To be calculated | 1.49 | To be calculated | 2.5
6 | 4 | 1.76 | 0.44 | 1.7493 (calculated in the positive moment design)
6 | To be calculated | 1.51 | To be calculated | 3.5

## Slide 15
3.2 Structural Design (continued)
Repartition of the columns (2D)

## Slide 16
3.2 Structural Design (continued)
Repartition of the columns (3D)

## Slide 17
3.2 Structural Design (continued)
Results of Moments Repartitions (3D)

## Slide 18
3.2 Structural Design (continued)
Results of Torsion Forces (3D)

## Slide 19
Results of Shear Forces (2D)
3.2 Structural Design (continued)

## Slide 20
Results of Restraint Reactions (3D)
3.2 Structural Design (continued)

## Slide 21
Deformed shape of slabs (3D)
3.2 Structural Design (continued)

## Slide 22
Deformed shape of slab of 3
3.2 Structural Design (continued)

## Slide 23
3.2 Structural Design (continued)

## Slide 24
Stress in the different slabs (3D)
3.2 Structural Design (continued)

## Slide 25
Gravity load (3D)
3.2 Structural Design (continued)

## Slide 26
Layers | Depth (m) | Description | Number of blows (N) | Soil state | Height of layer (H) | f (unit skin friction)
Layer #1 | 0 – 7.2 | Poorly graded brown sand | 5 to 27 | Loose to medium dense | - | -
Layer #2 | 7.2 – 10.2 | Silty brown sand | 12 to100 | Medium to very dense | - | -
Layer #3 | 10.2 – 13.2 | Sandy silt light brown | 8 to 10 | Medium | 3 | 20
Layer #4 | 13.2 – 24 | Poorly graded sand | 20 to 100 | Medium to very dense | 11 | 30
Layer #5 | 24 – 30 (end of boring) | Sandy lean clay light brown | 100 | Hard | 6 | 50
4.1 Soil Profile
Deduced from Geotechnical and Environmental Co.Ltd
4- Foundation Design

## Slide 27
The problems encountered in this project are summarized as follows:
The water table at the half Moon area located in the ground surface.
The ground of the site (sand is loose and saturated state) is susceptible to liquefaction phenomenon.
4.2 Site Conditions

## Slide 28
Shallow foundations ( Dynamic Compaction)
Deep foundations (Piles)
4.3 Foundation Systems

## Slide 29
http://www.soffons.org/Soffons/soffons.nsf/Realisations/C5AF1C6F35D64898C125748E00285D18
http://www.keyword-suggestions.com/ZHJpdmVuIHBpbGVz/

## Slide 30
D (m) | Z (m) | B (m) | L (m) | γ (Kn/m3) | C (kPa) | Nq | N γ | qu (kPa) | qallow (kPa)
1.5 | 11.5 | 1.5 | 1.5 | 10 | 0 | 134.88 | 271.76 | 16619 | 5539
2 | 12 | 2 | 2 | 10 | 0 | 134.88 | 271.76 | 17026 | 5675
2.5 | 12.5 | 2.5 | 2.5 | 10 | 0 | 134.88 | 271.76 | 17434 | 5811
3 | 13 | 3 | 3 | 10 | 0 | 134.88 | 271.76 | 17842 | 5947
1.5 | 11.5 | 1.5 | 1.5 | 10 | 0 | 134.88 | 271.76 | 17288 | 5762
2 | 12 | 2 | 2 | 10 | 0 | 134.88 | 271.76 | 17696 | 5898
2.5 | 12.5 | 2.5 | 2.5 | 10 | 0 | 134.88 | 271.76 | 18103 | 6034
3 | 13 | 3 | 3 | 10 | 0 | 134.88 | 271.76 | 18511 | 6170
1.5 | 11.5 | 1.5 | 1.5 | 10 | 0 | 134.88 | 271.76 | 17957 | 5985
2 | 12 | 2 | 2 | 10 | 0 | 134.88 | 271.76 | 18365 | 6121
2.5 | 12.5 | 2.5 | 2.5 | 10 | 0 | 134.88 | 271.76 | 18773 | 6257
3 | 13 | 3 | 3 | 10 | 0 | 134.88 | 271.76 | 19180 | 6393
1.5 | 11.5 | 1.5 | 1.5 | 10 | 0 | 134.88 | 271.76 | 18627 | 6209
2 | 12 | 2 | 2 | 10 | 0 | 134.88 | 271.76 | 19034 | 6344
2.5 | 12.5 | 2.5 | 2.5 | 10 | 0 | 134.88 | 271.76 | 19442 | 6480
3 | 13 | 3 | 3 | 10 | 0 | 134.88 | 271.76 | 19850 | 6616
4.3.1 Shallow Foundations

## Slide 31
D (m) | Z (m) | qallow (kPa) | q column (kPa) | B (m)
1.5 | 11.5 | 5947 | 6130 | Not verified (5947<6130)
2 | 12 | 6170 | 6130 | B = 3m
2.5 | 12.5 | 6257 | 6130 | B ≥ 2.5m
3 | 13 | 6209 | 6130 | B ≥ 1.5m
4.3.1 Shallow Foundations (continued)

## Slide 32
 | D=0.325 m |  | D=0.4 m |  | D=0.5m |  | D=0.6m | 
Soiltype | Qs (KN) | Qp (KN) | Qs (KN) | Qp (KN) | Qs (KN) | Qp (KN) | Qs (KN) | Qp (KN)
Sandy silt | 61.3 | - | 75.4 | - | 94.2 | - | 113.1 | -
Poorly graded sand | 336.9 | - | 414.7 | - | 518.3 | - | 622 | -
Sandy clay | 306.3 | 180.9 | 377 | 274 | 471.2 | 428.1 | 565.5 | 616.5
Sum | 704.6 | 180.9 | 867.1 | 274 | 1083.8 | 428.1 | 1300.6 | 616.5
4.3.2 Deep Foundations

## Slide 33
 | Qu(KN) | Qallow (KN) | Ap(m2) | qu (kPa) | Qallow (kPa)
D=0.325m | 885.4 | 295.1 | 0.083 | 10667.46 | 3555.42
D=0.4m | 1141.1 | 380.3 | 0.1257 | 9077.96 | 3025.45
D=0.5m | 1511.9 | 503.9 | 0.197 | 7674.61 | 2557.86
D=0.6m | 1917.1 | 639 | 0.283 | 6774.20 | 2257.95
4.3.2 Deep Foundations (continued)

## Slide 34: 5- Conclusion
The general conclusion drawn from this project can be summarized as follows:
A multistory hotel was developed and designed in a the Half-Moon Area. The site of the project extends over an area of about 1870 m2. It is composed of twelve floors including three underground car parking.
A structural design using computer software (ETABS) was performed on the hotel superstructure in order to determine the appropriate reinforcements and the different solicitations transmitted to the foundations systems.

## Slide 35: 5- Conclusion
A geotechnical investigation was carried out in order to select and design the appropriate Foundation System.
Two types of foundation system were adopted for this project, including shallow foundations when the area subjected is subjected to dynamic compaction and deep foundations (i.e. driven piles).