## Slide 1: Prince Mohammad bin Fahd University College of Engineering Department of Mechanical Engineering
Name: ID:
Faris Alzahrnai 201301367
Mohammad Al Sulaiman 201302093
Talal Alsadhan 201301178
Abdulaziz Alomar 201200090
Mohammad Alboroshaid 201302350
Design of a Miniature Wind Turbine for Automobiles
TEAM 3
Advisor:
Dr. Nader Sawalhi
Co-Advisor:
Dr. Muhammad Asad

## Slide 2: Outline
Objectives
Motivation and Relevance
Engineering Constrains, Design Specifications, and Engineering Standards
Conceptual Design, Attachment, and Theoretical Calculations
Testing
Results
Future Recommendations

## Slide 3: Objectives
Design of a miniature wind turbine to charge spare batteries for automobile
Use clean energy to produce power at minimal cost
Harvest wind energy, during drive of automobiles

## Slide 4: Motivation and Relevance
Design and manufacture of the wind turbine to be installed on automobiles
Help drivers, especially truck drivers
The main components of the system

## Slide 5: Design Constraints
Size of the system
Weight of the system
Sustainability

## Slide 6: Engineering Standards
Components | Engineering Standard | Details
Screw | ANSI metric | B18.2.3.2M - Formed hex screw, M16 x 2.0 x 80 --38CS
Bearing | NSK | Deep Groove Ball Bearing 6300ZZ 10mm I.D, 35mm O.D
Alternator | Delco-Remy | DRA3053

## Slide 7: 3D Model of the Design

## Slide 8: Design Specifications
Selected Material | Size | Item
Fiberglass | 590 mm | Inlet Nozzle (width)
Fiberglass | 250 mm | Outlet Nozzle (Width)
Fiberglass | 310 mm | Diameter of the fan cavity
1023 Carbon Steel Sheet | 3 mm | Thickness of the blades
1023 Carbon Steel Sheet | 12 | Number of the blades
 | 22 kg | Weight of the system
1023 Carbon Steel Sheet | 120 mm | Width of the fan blade
1023 Carbon Steel Sheet | 190 mm | Length of the fan blade

## Slide 9: Some insight into Conceptual Design
The area of the nozzle

## Slide 10: Some insight into Conceptual Design
The blades of the fan

## Slide 11: Attachments:
The way to stable the system
Other options
Some insight into Conceptual Design

## Slide 12: Theoretical Design Calculations
A) The outlet velocity C2: We have the speed of the inlet velocity which will be the speed of the air:
C1 = 100 km/h = 27.78 m/s T02 = T01 = 293 oK “Adiabatic process”
T01 =20oC=293 0K A2 =0.026m2 A1 = 0.062 m2 C2 = ? “the outlet velocity” P01 = 101320 Pa (1.0132 bar)
C2 = 67.33 m/s

## Slide 13: Theoretical Design Calculations
B) The wind power Pv
= 1.182 kg/m3 “the pressure at the outlet nozzle”
Av= 0.026 m2 “the outlet area which is directed to the fan”
u = 67.33 m/s “the outlet velocity of the nozzle when the air speed is 27.78 m/s = 100 km/hr”
Pv =
Pv = 4690.15 Watt

## Slide 14: Theoretical Design Calculations
C) Summary of the calculations
 | Wind Velocity |  |  | 
The required results | 60 km/hr | 80 km/hr | 100 km/hr | 120 km/hr
Inlet velocity of the nozzle (C1) | 16.67 m/s | 22.22 m/s | 27.78 m/s | 33.33 m/s
Outlet velocity of the nozzle (C2) | 40.09 m/s | 53.74 m/s | 67.33 m/s | 81.88 m/s
Angular speed (RPM) | 2466 | 3087 | 4315 | 4935
The wind power (Pv) | 1000.97 W | 2390.86 W | 4690.15 W | 7764.36 W

## Slide 15: Final Results
Wind Velocity (km/hr) | Voltage (V) | Current (A) | Electrical Power (W) | Wind Power (W) | Coefficient of Power (%)
60 | 14.63 | 10.04 | 146.8852 | 1000.97 | 14.67428594
80 | 29.76 | 15.42 | 458.8992 | 2390.86 | 19.19389676
100 | 64.52 | 19.32 | 1246.5264 | 4690.15 | 26.57753803
120 | 90.22 | 27.79 | 2507.2138 | 7764.36 | 32.29131313

## Slide 16: Experimental Testing and Sensors
A) Tachometer
B) Voltmeter

## Slide 17: Results
Chart: Wind Velocity vs Output Power
| 60 | 80 | 100 | 120
Output Power | 146.8852 | 458.8992 | 1246.5264 | 2507.2138
Chart: Wind Velocity vs Coffiecient of Power
| 60 | 80 | 100 | 120
Coefficient of Power (%) | 14.6743 | 19.1939 | 26.5775 | 32.2913

## Slide 18: Future Recommendations
Suggested Ideas

## Slide 20
THANK YOU FOR LESTINING 