## Slide 1: Learning outcome assessment III Spring 2020 (Final Presentation) The Design of 10-Lane Highway From Thuwal to Makkah

## Slide 2
Presented by:
Ahmad Al Rashid - 201100642
Mobarak jawah – 201401980
Ali Altamimi – 201303785
Abdulrahman Alotaibi – 201403009
Supervised by:
Dr. Mohammad Ali Khasawneh
Engr. Mohd Nayeemudin
Coordinator:
Dr.Andi Asiz

## Slide 3: OUTLINE
Introduction
Objectives
Location
Methodology
Constraints
Traffic Analysis
Geometric Design
  Horizontal Curves
  Vertical Curves
Soil Studies
  Soil Classification
  California Bearing Ratio
Structural Design
Drainage System
Interchange and Intersection Design
  AASHTO Standard
  Road Cross-Section
Cost Estimation
Civil 3D Technology (Short Clip)
Conclusion
References

## Slide 4: INTRODUCTION
Current roads in Makkah
Preparing for The Future
The Importance of this project
The highway starts from Thuwal, north of Jeddah, passes through the new eastern neighborhoods of Jeddah, and heads to the northern west of Makkah city.

## Slide 5: OBJECTIVES
A more organized distribution of permanent traffic volume between Thuwal and Makkah Al-Mukarramah.
Reducing traffic congestion on the Jeddah Makkah Highway
Traffic service towards Jeddah International Airport.
Facilitating commercial movement and movement of goods.
Facilitating industrial movement, and contributing to reducing the time period for the transportation of its products.

## Slide 6: LOCATION
Figure [1] - Topographic map, © OpenStreetMap contributors.
N
Makkah
Jeddah
Thuwal

## Slide 7: LOCATION
Suggested Options
Figure [2] - Suggested Options

## Slide 8: ALTERNATIVES
Table [1] - Alternatives
Three models have been developed and compared to the following figure:
Alternatives | Road Length (Km) | Number of Vertical Curves | Number of Horizontal Curves | Maximum cut height | Maximum fill height
1-Orange | 115.51 | 14 | 12 | 3.6 | 3.4
2-Blue | 97.34 | 24 | 17 | 9.5 | 9.7
3-Yellow | 101.11 | 31 | 62 | 18 | 21.5

## Slide 9
Methodology
Data Collection
Highway capacity analysis
Geometric Design
Soil study
Structural Design
Drainage system
Interchage and intersection Design
Cross section
Cost estimation
Completion of the project

## Slide 10: CONSTRAINTS
Community and Private Assets
Effects on All Travellers
Geology, Soils, Contaminated Land and Groundwater
Road Drainage and the Water Environment
Ecology and Nature Conservation

## Slide 11: Traffic Analysis
Average Daily Traffic
Future Average Daily Traffic

## Slide 12: Whereas: (ADT)d.y = The volume of current traffic.
Average Traffic for one week |  |  |  |  |  |  |  |  |  |  |  |  | 
JEDDAH-MAKKAH |  |  |  |  |  |  |  |  |  |  |  |  | 
Time | PC | PUCK UP | JEEP MODEL | TRUCKS |  |  |  |  | SMALL BUS | BIG BUS | MOTOR CYCLE |  | TOTAL
 |  |  |  | 2 LIGHT | 2 HEAVY | 3 | 4 | 5 |  |  |  |  | 
Avr. | 14224 | 5137 | 6421 | 356 | 125 | 11 | 21 | 11 | 749 | 500 | 135 |  | 27690
Avarage Traffic for one week |  |  |  |  |  |  |  |  |  |  |  |  | 
MAKKAH-JEDDAH |  |  |  |  |  |  |  |  |  |  |  |  | 
Time | PC | PUCK UP | JEEP MODEL | TRUCKS |  |  |  |  | SMALL BUS | BIG BUS | MOTOR CYCLE |  | TOTAL
 |  |  |  | 2 LIGHT | 2 HEAVY | 3 | 4 | 5 |  |  |  |  | 
Avr. | 13766 | 4917 | 5601 | 363 | 154 | 17 | 34 | 18 | 665 | 367 | 155 |  | 26056
TOTAL |  |  |  |  |  |  |  |  |  |  |  |  | 
(ADT)d.y | 27990 | 10054 | 12022 | 719 | 279 | 28 | 55 | 29 | 1414 | 867 |  | 290 | 53746
Table [2] – (ADT)d.y
Traffic Analysis: Average Daily Traffic

## Slide 13
Avarage Traffic for one week |  |  |  |  |  |  |  |  |  |  |  |  | 
JEDDAH-MAKKAH |  |  |  |  |  |  |  |  |  |  |  |  | 
Time | PC | PUCK UP | JEEP MODEL | TRUCKS |  |  |  |  | SMALL BUS | BIG BUS | MOTOR CYCLE |  | TOTAL
 |  |  |  | 2 LIGHT | 2 HEAVY | 3 | 4 | 5 |  |  |  |  | 
Avr. | 14224 | 5137 | 6421 | 356 | 125 | 11 | 21 | 11 | 749 | 500 | 135 |  | 27690
Avarage Traffic for one week |  |  |  |  |  |  |  |  |  |  |  |  | 
MAKKAH-JEDDAH |  |  |  |  |  |  |  |  |  |  |  |  | 
Time | PC | PUCK UP | JEEP MODEL | TRUCKS |  |  |  |  | SMALL BUS | BIG BUS | MOTOR CYCLE |  | TOTAL
 |  |  |  | 2 LIGHT | 2 HEAVY | 3 | 4 | 5 |  |  |  |  | 
Avr. | 13766 | 4917 | 5601 | 363 | 154 | 17 | 34 | 18 | 665 | 367 | 155 |  | 26056
TOTAL |  |  |  |  |  |  |  |  |  |  |  |  | 
(ADT)d.y | 27990 | 10054 | 12022 | 719 | 279 | 28 | 55 | 29 | 1414 | 867 |  | 290 | 53746
(ADT)b.y | 61330 | 22030 | 26342 | 1575 | 611 | 61 | 121 | 64 | 3098 | 1900 |  | 635 | 117764
FACTOR (T). | 1 | 1.25 | 1.25 | 1.50 | 2.00 | 2.50 | 3.00 | 3.00 | 1.30 | 2.25 |  | 0.50 | 
(ADT)b.y | 61330 | 27537 | 32927 | 2363 | 1223 | 153 | 362 | 191 | 4028 | 4274 |  | 318 | 134705
Table [3] – (ADT)b.y
Traffic Analysis: The Volume of Future Traffic (20 Years)
(ADT)F = (ADT)P*(1+GF)^20 *FACTOR (T)

## Slide 14: Traffic Analysis: Road Capacity

## Slide 15
Geometric Design: Horizontal Curves
Purpose:
To provide change in direction to the centre line of a road.
Process:
When a vehicle transverse a horizontal curve, the centrifugal force acts horizontally outwards through the center of gravity of the vehicle.

## Slide 16: The geometric quality of road when seen from above in “plane” view.
Geometric Design: Horizontal Alignment
Plane View:
Figure [3] Plane View
Figure [4]: Road in Tabuk, Saudi Press Agency.

## Slide 17
The centrifugal force acting on a vehicle
passing through a horizontal curve
has two effects:
  Overturning Effect
  Transverse Skidding Effect
Figure [5] Superelevation
P = W V2 / g R
Geometric Design: Superelevation

## Slide 18: Geometric Design: Simple Curve
PC
PT
Circular Curve
Tangent
Point of Curvature
Point of Tangency

## Slide 19
Geometric Design: Elements of Horizontal Curves

## Slide 20
PC
PT
PI
T
Direction
-PI: Point of Intersection
-PC: Point of Curvature
-PT: Point of Tangency
-T: Tangent Length

## Slide 21
L
LC
R
R
  R: Radius of Curve
  LC: Length of Curve
  L: Chord Length

## Slide 22


M
E
/2
  : Deflection Angle
  E: External ordinate
  M: Middle ordinate

## Slide 23
Geometric Design: Horizontal Curves in The Project
First Curve details
Station (0+00) | Θ (deg) | X (m) | Y (m) | L’ (m)
115+40 | 0° | 0 | 0 | 0
115+60 | 2.076° | 49.99 | 0.9057 | 100
115+80 | 4.152° | 99.9 | 3.6218 | 200
116+00 | 6.227° | 149.622 | 8.142 | 300
116+20 | 8.304° | 199.11 | 14.47 | 400
116+40 | 10.38° | 253.32 | 22.6 | 500
116+80 | 12.46° | 297.74 | 32.5 | 600
117+00 | 14.53° | 346.22 | 44.137 | 700
117+20 | 16.61° | 394.48 | 57.6 | 800
117+24 | 16.87° | 400.47 | 59.387 | 812.31
Table [4]: 1st Curve

## Slide 24
Second Curve details
Station (0+00) | Θ (deg) | X (m) | Y (m) | L (m)
167+40 | 0° | 0 | 0 | 0
167+60 | 1.87° | 49.92 | 0.815 | 100
167+80 | 3.74° | 99.8 | 3.26 | 200
168+00 | 5.62° | 149.83 | 7.354 | 300
168+20 | 7.49° | 199.44 | 13.05 | 400
168+40 | 9.36° | 248.83 | 20.37 | 500
168+60 | 11.24° | 298.22 | 29.35 | 600
168+79.85 | 13.10° | 346.77 | 39.82 | 699.285
Table [5]: 2nd Curve

## Slide 25: The 1st Procedure in Alignment was Stationing
Graph [1]: Vertical Alignment
Geometric Design: Vertical Alignment
Notes: Therefore, roads will almost always be a bit longer than their stationing because of the vertical alignment
Draw in stationing on each of these curves and explain it

## Slide 26
Definition:
  It is the elevation or the profile of the center line of the road
Objective:
-Determine elevation to ensure:
    Proper drainage
    Acceptable level of safety
Primary challenge
  Transition between two grades
  Vertical curves detail
  Quantity of cut and fill
G1
G2
G1
G2
Crest Vertical Curve
Sag Vertical Curve

## Slide 27: Geometric Design: Cut and Fill Quantities
Graph [2] Cut and Fill

## Slide 28: Geometric Design: Maximum Grades for Urban and Rural Highways
Table : Urban and Rural Freeways

## Slide 29: Geometric Design: Maximum Grades for Local Road and Street
Table Local Roads

## Slide 30
Source: Iowa DOT Design Manual
Note: L is measured from here to here
Not here
PVC
PVI
PVT

## Slide 31
Geometric Design:
Vertical Curves in the project
First Curve details
Point | X | Station | Y | Elevation
PVC | 0 |  | 0 | 227.345
1 | 30 |  | 0.055 | 228.285
2 | 60 |  | 0.22 | 229.000
PVI | 90 |  | 0.495 | 230.000
4 | 120 |  | 0.88 | 230.115
5 | 150 |  | 1.375 | 230.340
PVT | 180 |  | 1.98 | 230.675
Table [6] Curve Details

## Slide 32
Geometric Design:
\Vertical Curves in the project
Second Curve details
Point | X | Station | Y | Elevation
PVC | 0 |  | 0 | 
1 | 25 |  | 0.0687 | 230.700
2 | 50 |  | 0.275 | 230.965
3 | 75 |  | 0.62 | 231.210
4 | 100 |  | 1.1 | 231.890
5 | 125 |  | 1.719 | 231.209
6 | 150 |  | 2.476 | 230.866
7 | 175 |  | 3.37 | 230.660
8 | 200 |  | 4.40 | 230.590
PVT | 209 |  | 4.807 | 230.557
Table [7] Curve Details

## Slide 33
SOIL STUDIES
Soil classification
Engineering classification systems:
  Textural Classification.
  AASHTO.
  Unified Soil Classification.
  The International Soil Classification.
  American Society of Testing Material.

## Slide 34
Soil Classification
First sample
Sieve NO. | Sieve open (mm) | Cumulative Reserved (gm.) | Cumulative Reserved (%) | Passing (%)
1.5" | 38.1 | 49.1 | 2.14 | 97.86
1" | 25 | 223.3 | 9.74 | 90.26
0.5" | 12.7 | 526.1 | 22.94 | 77.06
0.31" | 7.9 | 767.7 | 33.48 | 66.52
#4 | 4.75 | 1238.166 | 54 | 46
#10 | 2 | 1504.1 | 65.6 | 34.4
#16 | 1.18 | 1707.2 | 74.46 | 25.54
#18 | 1 | 1747.7 | 76.22 | 23.78
#35 | 0.5 | 1916.6 | 83.59 | 16.41
#40 | 0.425 | 1942.1 | 84.7 | 15.3
#50 | 0.355 | 2011.7 | 87.74 | 12.26
#80 | 0.18 | 2090 | 91.15 | 8.85
#200 | 0.075 | 2206.1 | 96.21 | 3.79
Pan | 0 | 2292.9 | 100 | 0
A-2-7
Chart: Sieve (mm)
| 38.1 | 25 | 12.7 | 7.9 | 4.75 | 2 | 1.180000000000001 | 1 | 0.5 | 0.42499999999999999 | 0.35499999999999998 | 0.18 | 7.4999999999999997E-2 | 0
 | 97.86 | 90.26 | 77.06 | 66.52 | 46 | 34.4 | 25.54 | 23.78 | 16.41 | 15.3 | 12.26 | 8.85 | 3.79 | 0
Graph [3] 1st Sample

## Slide 35
Second Sample
A-1-b
Sieve NO. | Sieve open (mm) | Cumulative Reserved (gm.) | Cumulative Reserved (%) | Passing (%)
1.5" | 38.1 | 0 | 0 | 100
1" | 25 | 323.6 | 8.99 | 91.01
0.5" | 12.7 | 817.7 | 22.71 | 77.29
0.31" | 7.9 | 1289.4 | 35.82 | 64.18
#4 | 4.75 | 1727.95 | 48.1 | 51.9
#10 | 2 | 2354.1 | 65.39 | 34.61
#16 | 1.18 | 2550.9 | 70.86 | 29.14
#18 | 1 | 2591.5 | 71.99 | 28.01
#35 | 0.5 | 2805.4 | 77.93 | 22.07
#40 | 0.425 | 2884.7 | 80.13 | 19.87
#50 | 0.355 | 2964.1 | 82.34 | 17.66
#80 | 0.18 | 3118.8 | 86.64 | 13.36
#200 | 0.075 | 3405.3 | 94.59 | 5.41
Pan | 0 | 3599.9 | 100 | 0
Chart: Sieve (mm)
| 38.1 | 25 | 12.7 | 7.9 | 4.75 | 2 | 1.180000000000001 | 1 | 0.5 | 0.42499999999999999 | 0.35499999999999998 | 0.18 | 7.4999999999999997E-2 | 0
 | 100 | 91.01 | 77.29 | 64.18 | 51.9 | 34.61 | 29.14 | 28.01 | 22.07 | 19.87 | 17.66 | 13.36 | 5.41 | 0
Graph [4] 2nd Sample

## Slide 36
Third Sample
A-1-b
Sieve NO. | Sieve open (mm) | Cumulative Reserved (gm.) | Cumulative Reserved (%) | Passing (%)
1.5" | 38.1 | 147.5 | 5.04 | 94.96
1" | 25 | 261.1 | 8.92 | 91.08
0.5" | 12.7 | 624.3 | 21.34 | 78.66
0.31" | 7.9 | 803.5 | 27.46 | 72.54
#4 | 4.75 | 1273.8 | 43.54 | 56.46
#10 | 2 | 1514.8 | 51.78 | 48.22
#16 | 1.18 | 1838.6 | 62.84 | 37.16
#18 | 1 | 191.8 | 65.38 | 34.62
#35 | 0.5 | 2249.5 | 76.89 | 23.11
#40 | 0.425 | 2354.7 | 80.48 | 19.52
#50 | 0.355 | 2475 | 84.6 | 15.4
#80 | 0.18 | 2666 | 91.12 | 8.88
#200 | 0.075 | 2892.6 | 98.87 | 1.13
pan | 0 | 2925.7 | 100 | 0
Chart: Sieve (mm)
| 38.1 | 25 | 12.7 | 7.9 | 4.75 | 2 | 1.180000000000001 | 1 | 0.5 | 0.42499999999999999 | 0.35499999999999998 | 0.18 | 7.4999999999999997E-2 | 0
 | 94.96 | 91.08 | 78.66 | 72.54 | 56.46 | 48.22 | 37.16 | 34.62 | 23.11 | 19.52 | 15.4 | 8.88 | 1.13 | 0
Graph [5] 3rd Sample

## Slide 37
Soil Study: Californian Bearing Ratio (CBR)
Figure [7] CBR Test

## Slide 38
CBR Test Results
 | Moisture Content (%) | Compaction (%) | CBR (%) | 
First Sample | 15.5 | 99.2 | 22.2 | 
Second Sample | 17.4 | 99.5 | 16 | 
Third Sample | 12.96 | 99.6 | 25 | 
Table [7] CBR Test Results

## Slide 39
Structural Design: Layer Thickness of Pavements
Highway Pavements Design Methods
  AASHTO guide method
  The Asphalt Institute )T. A. I. Method(
  Portland Cement Association (PCA)
  N. C. S. A. (National Crushed Stone Association).
  MEPDG (Mechanistic-Empirical Pavement Design)

## Slide 40: Structural Design: AASHTO Design Equation
W18 = design traffic (18-kip ESALs)
ZR = standard normal deviate
So = combined standard error of traffic and performance prediction
DPSI = difference between initial and terminal serviceability index
MR = resilient modulus (psi)
SN = structural number
Structural Number

## Slide 41: Structural Design: AASHTO Design Equation
Inputs
  Design life (analysis period)
  Traffic (W18)
  Foundation stiffness (MR)
  Performance criterion (PSI)
  Reliability (ZR, So)
Outputs
  Required pavement capacity: Structural Number (SN)

## Slide 42: Assuming Structural details:
Surface a1 = 0.42 (Modulus E = 4.3)
Base a2 = 0.13 (C. B. R. = 80%)
Subbase a3 = 0.095 (C. B. R. = 20%)
(AC) | Sub.B (Sand-gravel) | B.C (Crushed Stone) | Layer
Marshall (Stability) (1900 Ib) | 20% | 80% | CBR%
Flexibility ( 40000 psi ) | 16500 | 28500 | Mr(psi)
0.42 | 0.095 | 0.12 | a
Table [8] Pavement Design
Structural Design: AASHTO Design Equation

## Slide 43
Figure [8] Design Chart (AASHTO, 1993)
SN:a1d1+ a2d2m2+a3d3m3

## Slide 44
SN1=1.95
Sn2=2.82
Sn3=3.78
D1= 4.72 in
D2= 7.87 in
D3= 7.87 in
Structural Design:
Thickness of Layers
Figure [9] Layers

## Slide 45
Drainage system
(Design objectives)
Reduce waterlogging.
Control salinity.
Make new land available for agriculture.
Reduces the amount of water stored on or in the soil.
Introduces a flow rate of water through the system.
Disturbance and/or pollution of the environment.
Depletion and/or over-exploitation of the natural resources.
Destruction and/or impairment of the natural ecosystem.

## Slide 46
Box Culverts
(Application)
Short-span bridges (over highways, waterways,
railways, for golf courses, etc.)
Conveyance of storm water, sewage or industrial
wastes (storm drains)
Tunnels (to house conveyers, utilities, etc.; to provide
access, escape routes, etc.
Detention

## Slide 47
Drainage System: Basin Area
The figure shows the basin area And it includes (its area - its inclination - the highest level - the longest level - the longest waterway), and it has been found from the topographical maps and it is shown in the following table
Figure [10] Basin Area

## Slide 48
ID | STATION | AREA (m2) | Lowest Elevation (m) | Highest Elevation (m) | Length (m) | Slope
1 | 892+12 | 2103 | 248 | 210.5 | 756 | 0.05
2 | 898+56 | 1980 | 247 | 202.9 | 708 | 0.0622
Basin Area Details:
ID | STATION | Runoff Coefficient | Design Flow /sec)
1 | 892+12 | 0.5 | 39.43
2 | 898+56 | 0.45 | 31.68
ID | STATION | Runoff Coefficient | 
1 | 892+12 | 0.5 | 39.43
2 | 898+56 | 0.45 | 31.68
/sec) Eq(8.1)
Determination of Inflow:
Table [9] Basin Area Details
Table [10] inflow
Drainage System: Basin Area

## Slide 49
ID | STATION | No. of openings in culverts | Type of culverts | Highest (m) | Width (m) | Slop | According to the size of culverts /sec) | 
1 | 892+12 | 2 | Box culvert | 2 | 1.5 | 39.43 | 39.43 | 
2 | 898+56 | 2 | Box culvert | 1.5 | 1 | 31.69 | 31.69 | 
ID | STATION | No. of openings in culverts | Type of culverts | Highest (m) | Width (m) | Slop |  | 
1 | 892+12 | 2 | Box culvert | 2 | 1.5 | 39.43 | 39.43 | 
2 | 898+56 | 2 | Box culvert | 1.5 | 1 | 31.69 | 31.69 | 
Height of the water:
Area determined form equation:
Determine the width of culvert:
Table [11] Dimensions

## Slide 50
Box Culverts Cross Section
After studying the rainfall, and the inflow rate, the suggested box culvert cross section consists of 2 opening, such as this photo.
Figure [11] Box Culverts, SPA, Jeddah

## Slide 51: Basic Principles of Interchange (Design Objectives)
Reduce the number of conflict points
Minimize severity of potential conflicts
Provide for smooth flow of traffic
Consider both vehicles and pedestrians
Avoid multiple and compound merging and diverging

## Slide 52
Intersection Control
Conflict Points at Intersections
Crossing conflicts, however, tend to have the most severe effect on traffic flow and should be reduced to a minimum whenever possible.

## Slide 53: Design Vehicles
Set of 20 design vehicles with standard physical dimensions according to AASHTO

## Slide 54: Road Intersection lanes
Using the division of the intersection into several tracks and analyzing the traffic volume for each of the tracks and their statistics, the intersection is designed to be two lanes for each movement path
Figure [13] Road Lanes

## Slide 55
Path | PC | Bus | Trailer | Motorcycle
1 | 65.5% | 32.1% | 2.7% | 0.65%
3 | 74.2% | 21.1% | 4.7% | 0%
4 | 74% | 21.1% | 3.2% | 1.87%
6 | 73.7% | 18.55% | 7.73% | 2%
7 | 80% | 14.88% | 4.1% | 1.3%
9 | 70.1% | 23.1% | 5.9% | 0%
10 | 76.8% | 19.3% | 3.4% | 0%
12 | 67.7% | 27.2% | 4.6% | 0%
Then the percentage for each vehicles types in each path:
The study was conducted during daylight hours between 8 a.m. to 9 a.m., the following table shows the traffic count statistics for each type of vehicle:
Table [12] Percentage of Vehicles

## Slide 56: Intersection Design: Calculations
Accordaing to Highway Capacity Manual (HCM), the capacity of entry equal to:
Single line = 762 veh/lane.
Urban compact = 608 ceh/lane.
So, based on the project is an urban compact road, and by using tha maximum traffic volume value, then the number of lanes equal to
Path | Fhv | Total
1 | 1.221 | 781
3 | 1.156 | 613
4 | 1.124 | 780
6 | 1.185 | 460
7 | 1.102 | 512
9 | 1.163 | 512
10 | 1.128 | 683
12 | 1.18 | 875
Table [14] PCE
Path | PC | Bus | Trailer | Motorcycle | Fhv
1 | 0.655 | 0.48 | 0.054 | 0 | 1.221
3 | 0.742 | 0.32 | 0.094 | 0 | 1.156
4 | 0.74 | 0.32 | 0.064 | 0 | 1.124
6 | 0.74 | 0.28 | 0.1546 | 0 | 1.185
7 | 0.8 | 0.22 | 0.082 | 0 | 1.102
9 | 0.7 | 0.345 | 0.118 | 0 | 1.163
10 | 0.77 | 0.29 | 0.068 | 0 | 1.128
12 | 0.677 | 0.41 | 0.092 | 0 | 1.18
Table [13] Fhv Values
Then, PCE for each path:
Total traffic volume:

## Slide 57: Road Cross-Section
The cross section of the road consists of different elements:
  Paved road surface.
  Road lanes.
  Cross slop.
  Shoulders.
  Sidewalks.

## Slide 58: Cost Estimation
Cost Estimaition Definition
  It is a study of the cost of the project, and the economic dependencies of the project, on the state and on the consumer.
Cost Estimation Criteria:
  Cut and fill quantities.
  Leveling of ground.
  Material price.
  Equipment work time.
  Labors price.
  Management cost.
  External expenses

## Slide 59
Item | Item deception | Unit | Quantity | Unit Price (SR) | Total
1 | Cutting and back filling the natural land according to the survey plans, including the deportation of the excess, and the supply of the minus, to reach the paving level, according to the instructions of the consulting engineer. | M2 | 7620270 | 65 | 495317550
2 | Supply and install of Sub-grade layer to get to a level of deigned Sub-base level including stake out, and compact it, to get 98% compaction degree at standard proctor test. | M3 | 2618952 | 22 | 57916944
3 | Supply and install sub-base layer, 20cm thickness according to design specification, not less than 40% CBR test, including compaction not less than 98% at standard proctor test according to instruction from consultant engineer. | M3 | 1500396 | 38 | 57015025
4 | Supply and install Base-cores layer, 20cm thickness according to design specification, not less than 80% CBR test, including compaction not less than 98% at standard proctor test according to instruction from according to instruction from consultant engineer. | M3 | 1500396 | 52 | 78020592
Cost Estimation: Item Cost Analysis
Table [15a] Cost Estimation

## Slide 60
Item | Item description | Unit | Quantity | Unit Price SR | Total
5 | Supply and install MC1 layer, according to design specification and according to instruction of consultant engineer. | M2 | 7501977 | 2.5 | 18754942
6 | Supply and install asphalt layer, 7 cm thickness, including compaction, not less than 98%, and not less than 1900 lb stability and not less than 40000 psi flexibility, according to design specification and according to instruction of consultant engineer. | M2 | 7501977 | 22 | 165043494
7 | Supply and install RC2 layer, according to design specification and according to instruction of consultant engineer. | M2 | 7501977 | 2.5 | 18754942
8 | Supply and install asphalt layer, 5 cm thickness, including compaction, not less than 98%, and not less than 1900 lb stability and not less than 40000 psi flexibility, according to design specification and according to instruction of consultant engineer. | M2 | 7501977 | 14 | 105027678
Total |  |  |  |  | 995851167
Table [15b] Cost Estimation

## Slide 61: Cost estimation: Total Cost
By calculating the cost of materials and asking several contractors and analyzing prices into business items, Total cost price equal to = 995851167 + 10% Staff Cost.
The overall project value is estimated = 1095436284 SR.

## Slide 62: AutoDesk Civil 3D Technology

## Slide 64: REFERENCES

## Slide 65
THANK YOU FOR LISTENING