## Slide 1: College of Computer Engineering and Science (CCES) ASSE 4311- Learning Outcome Assessment III - CE Section: 210 Agriculture Assistant Drone (AAD)
Maysoon Alfares 201400842 Computer Engineering
Ghadeer Alsoghair 201403330 Computer Engineering
Shoug Alhajri 201402622 Computer Engineering
Amjad Alkhathlan 201502035 Computer Engineering
Advisor:
Dr. Loay Alzubaidi

## Slide 2: Outlines
Introduction
Objectives
Project Specification
Requirement Specification
Hardware Components
Software Components
Constraints
Design
First Conceptual Design
Second Conceptual Design
Hardware Design
Software Design
Prototype Development
Aircraft Body
Creating 3D Design
Arduino UNO
Image Recognition
Stages of Applying Image Recognition
Comparison of Image Recognition in Raspberry Pi and PC
Setup Modules Communication
Xbee Setup Configuration
Test AT mode to AT mode
Test AT mode to API mode

## Slide 3: Cont’d
Test and Verification
Module Testing
System Testing
Limitations
Future Recommendations
Conclusion

## Slide 4: Introduction:
Problem Statement

## Slide 5
Online Interview

## Slide 6: Objectives
Help in improving agriculture environment facilities.
Apply new technologies for estimating the number of palm trees in a field.
Enhance people’s knowledge regarding different applications of drones.
Contributing in creating sustainable palm tree fields, to protect and
increase the economy of dates production.

## Slide 7: Specification:
Image Recognition
Spraying Operation
Notes: shoug

## Slide 8: Survey:

## Slide 9: Requirement Specification:
1
Functional Requirement
Performance
Controllability
Reliability
Safety
Accuracy
Detection
2
Nonfunctional Requirement
Flight Time
Weight
Distance
Detection
Reliability
Notes: shoug

## Slide 10
Wireless communication.
Performance
Functional Requirement
Controllability
The arm spray with the buttons
Reliability
Safety
The arm responding.
Avoid any collision with drone propellers
Results of palm trees recognition
Captured different areas
Accuracy
Detection

## Slide 11
25 minutes
Flight Time
Nonfunctional Requirement
Weight
Weight of the drone: 1.043 kg Weight of the 3D arm: 0.467 kg Weight of the Raspberry Pi: 0.139 kg Total Weight: 1.649 kg
Payload : 1 Kg
Distance
Detection
Exceeds about 1640 ft. (500 m)
Detecting only palm trees.
Total weight
Reliability

## Slide 12: Use Case Diagrams:

## Slide 13: Use Case Diagrams:

## Slide 14: Hardware Components:
Arduino UNO
Power Bank
Raspberry Pi
Pushbutton
Xbee
Mini breadboard

## Slide 15: Hardware Components:
Servo Motor
Pi Camera
PC

## Slide 16: Software Components:
Arduino
XCTU
Python
Trello
Google
StarUML
LabelImg

## Slide 17: Constraints:
Technical:
Arduino IDE, Raspberry pi, Python.
New components.
Time:
Unavailable components
Building robotic arm
Testing
Cost
Components
Printing
Physical:
Drone , Xbee
Design:
Select the components probably
05
01
02
03
04

## Slide 18: Conceptual Design:
Drone: DJI Phantom 3
Cameras
IR Distance Sensor
XBee
Ultrasonic Sensor
RC (Transmitter and Receiver)
GPS
Arduino UNO
MPU-9520
Battery
Flex Sensor (Spectra Symbol 2.18’’)
First Conceptual Design

## Slide 19: Conceptual Design:
Flex Sensor
MPU-6050
Two servo motors (micro servo)
Xbee (Transmitting/ Receiving)
Second Conceptual Design

## Slide 20: Hardware Design
Implementation

## Slide 21
Receiver Circuit

## Slide 22
Transmitter Circuit

## Slide 23: Setting up Raspberry Pi
SD Card
•Formatting the SD card by using SD card formatter
Downloading the Raspbian Scratch OS
•Burning the Raspbian OS by using the Etcher open-source
keyboard, mouse, HDMI cable and the power should be inserted into the correct raspberry ports

## Slide 24: Setting up Pi camera
Enabling the camera

## Slide 25: Setting up Drones Camera

## Slide 26: Software design

## Slide 27: Arduino IDE
Arduino software Integrated Development Environment (Arduino Software IDE)
Easy to deal with
More applicable to implement with
Arduino is a stable open source electronics platform, with many libraries.
The user will find a lot of hardware that they can directly plug in, and immediately use it with an Arduino library.
It is useful to use it before implementing the actual PCB

## Slide 28: LabelImg
Graphical image annotation tool that is written in Python and uses Qt for its graphical interface.
This annotation are saved as XML files in PASCAL VOC format.
By using this tool the user will be able to label the needed object from the image

## Slide 29: Google Colaboratory
Free cloud service that supports GPU and TPU.
Using the Google Colaboratory programmers can improve their coding skills in Python programming language.
Can develop deep learning applications by using the popular libraries such as Keras, TensorFlow, and OpenCV.
Purpose to use for this project
Supports GPU
Uses Python
Easy to download needed dependencies

## Slide 30: Keras API
High level API
Is a specification for building models layer-by-layer that works with multiple frameworks
Designed to be inviting, flexible, and simple to learn
works as a wrapper which wraps the efficient libraries such as TensorFlow and then will allow to define and train neural network models in a few short lines of code

## Slide 31: Image Recognition
The ability of software to identify objects, places, people, writing and actions in a given image.
It is used to perform a large number of computer vision operations, such as labeling the content of images.
The software for image recognition requires deep machine learning which requires the system to be pre-trained with thousands of pre-labeled pictures
It can be performed better when using the convolutional neural network (CNN), and imagery
CNN is a class of deep neural networks, that is mostly applied for analyzing visual which consists of an input and an output layer, as well as multiple hidden layers

## Slide 32: Applying Image Recognition Dataset collection
Collecting a huge amount of palm trees images
Collected form Prince Mohammed University campus

## Slide 33: Applying Image Recognition Dataset Labeling
Labeling the object to identify the desired object and to separated it from other items.
By using the graphical image annotation LabelImg tool.

## Slide 34: Applying Image Recognition Dataset Labeling (Steps)

## Slide 36: Applying Image Recognition Training & counting
Google Colab is used with Python 3.6
GPU is enabled
Installing the high-level neural network API Keras

## Slide 37: Applying Image Recognition Training & counting(Coding)
Environment setup

## Slide 38: Applying Image Recognition Training & counting(Coding)
•Making Dataset

## Slide 39: Applying Image Recognition Training & counting(Coding)
•Training Model

## Slide 40: Applying Image Recognition Training & counting(Coding)
Testing

## Slide 41: Applying Image Recognition Training & counting (Coding)
Testing

## Slide 42: Applying Image Recognition Two Options
Raspberry Pi

## Slide 43: Applying Image Recognition Two Options
Personal Computer

## Slide 44: Prototype Development
Aircraft Body
Criteria | Details
Weight (Battery & Propellers Included) | 1216 g
Diagonal Size (Propellers Excluded) | 350 mm
Max Speed | 16 m/s (ATTI mode)
Max Flight Time | Approx. 25 minutes
Operating Temperature Range | 32° to 104°F (0° to 40°C)
Satellite Positioning Systems | GPS
Stabilization | 3-axis (pitch, roll, yaw)
Max Transmission Distance | FCC: 1000 m CE: 500 m (outdoors and unobstructed, aircraft's altitude at 400 feet (120 m))

## Slide 45
Creating 3D Design

## Slide 47
Set up Modules Communication
Xbee Setup Configuration

## Slide 48
1

## Slide 49
2

## Slide 50
3

## Slide 51
4

## Slide 52
AT Mode vs. API Mode

## Slide 53
Test AT mode to AT mode

## Slide 54
Once writing in router, it will show the writings as a blue colored in the router itself but going to show as red colored in the coordinator, and that means it came from the other Xbee. AT mode allowed to transmit and re-transmit communication, both router and coordinators are allowed to send to each other.

## Slide 55
Test AT mode to API mode
AT
API

## Slide 56: System Testing and Analysis
Modules Testing

## Slide 57: Testing Pi Camera
testing the Pi camera workability by using the following commands lines
For capturing a still image by using the command line in terminal (raspistill)
For capturing a still image with a specified format (jpg) (raspistill -o testshot.jpg)
For capturing a video with the used of raspivid command
For capturing a video by specifying the time limit with the used of (raspivid –o video.h264 -t 10000) command

## Slide 58: Testing Pi Camera
Testing the Pi camera with capturing an image of palm tree

## Slide 59
Arduino UNO Connection with Xbee Shield

## Slide 60: 2. System Testing

## Slide 61
Test 1: Aircraft Taking-Off

## Slide 63
Image Recognition Test

## Slide 64: Image Recognition Test
Low Accuracy
High Accuracy

## Slide 65
Test 3: Interactivity

## Slide 66
Test 4: Push/Release operation of the Spraying Operation Arm
Algorithm of push/release operation:
1\ Check interactivity between two Xbee has been configured, by looking to the led flashing mechanism, Tx flashes twice per sec, Rx flashes once per second.
2\ Move switch to Xbee mode
3\ Click push button
4\ Sends values through the serial port
5\ The servo motor Xbee shield takes the values from the serial port and move accordingly
6\ The top head of the arm will be pulled down and pressed the spray bottle and then spraying will done
7\ Click release button
8\ The top head of the arm will release and back to its original place, and then the spray bottle will stop spraying

## Slide 67
Pseudocode
Tx

## Slide 68
Tx

## Slide 69
Rx

## Slide 70
Rx

## Slide 71
Serial Port Monitor
Tx
Rx

## Slide 72
Serial Port Plotter

## Slide 73: Limitations:
Duplication in counting
Camera
Battery

## Slide 74: Future Work:
Using different components
Fire Sensor
Flame Detector:
Different Weather Conditions
Image recognition
Spraying technique
Profinaintilty applied to the robotic arm
Different Fields
Improve the Design
Real time video-based detection
Motion detection

## Slide 75: Conclusion
Thank you for listening