## Slide 1: Adjustable Single Weight Lifting Machine
Mechanical Engineering Senior Project
Group #12
Advisor: Ragu Kannan
Co Advisor: Nader Sawalhi

## Slide 2: Outline
Introduction
Objectives
Background
Design
Work Tasks
Challenges

## Slide 3: Introduction
Bodybuilding sport is highly diffused between people in all ages starting from 16 years old.
Lifting machines are so heavy, costly, take a lot of space in the gym and hard to be moved.
The Adjustable Single Weight Lifting Machine is our solution.
ASWLM is a machine that allows the user to lift different weights by using one weight bar only.

## Slide 4: Objectives
Inventing a new Idea Replaces the physical weight addition method.
Decrease the cost of GYM machines manufacturing.
Lightweight machines which can be carried everywhere.
Avoid injuries which may occur while changing the weight.
Decrease the space used for GYM equipment.

## Slide 5: Background
Machines Types
-Resistance Machines
-Cardiovascular Equipment

## Slide 6: Background
Sport types and exercise mechanisms
Horizontal Seated Leg Press Lat Pull-Down

## Slide 7: Background
Cable Biceps rope Seated Chest Press

## Slide 8: Background
Bicycle Gears

## Slide 9: Design
Overall design (Isometric View)
Height (170cm)
Width (64x75 cm)

## Slide 10: Design
Overall design (Top View)

## Slide 11: Design
Aluminum Cones
Ratio is 4:1
Small diameter (4 cm)
Large diameter (16 cm)
Shaft diameter (3 cm)
Shaft
Large diameter
Small diameter

## Slide 12: Design
Aluminum Cones (mechanism)

## Slide 13: Design
[W = FD]
W: Work
F: Force
D: Distance
1:4 | 4:1 | 1:1
37.5x F = 20kg x 150cm F = 80 kg | 37.5x F = 20kg x 9.4cm F = 5 kg | 37.5x F = 20kg x 37.5cm F = 20 kg
Calculations
The training arm will be lifted up to 60 cm to rotate the shaft 37.5 cm which is 4 times the circumference (9.4 cm) of the shaft (4 turns)
60 cm
37.5 cm
150 cm

## Slide 14: 1:4
4:1

## Slide 15: Testing and Results
Test Name | Date | Results
Arm Movement and Bearing Rotation | 16/05/17 | Was done Successfully
Con Pulley Movement | 16/05/17 | The cons rotate perfectly without any problem
Initial Test for the Whole System | 24/05/17 | Ropes material was not perfect
Final Test | 27/05/17 | Rope was changed, The machine worked fine
Testing Details
Friction Coefficients
Material | μ | Results
Rubber on Aluminum | 0.5 - 0.8 | We did not test it
Rubber on Wood | 0.6 - 0.851) | Succeeded

## Slide 16: Testing and Results
VIDEO

## Slide 17: Design Constrains
Economic | Manufacturability | Safety
Marketing analysis | Production of components | Operational
Manufacturing cost | Purchase of components | Human
Distribution costs | Assembly | 

## Slide 18: Work Tasks
Working on the Project Report
Buying aluminum Billets
Buying pulleys, Bearings, Belt and Ropes
Fabrication of the Aluminum Billets
Manufacturing the Steel parts
Assemble everything together
Testing and Review

## Slide 19: Future Improvements
Changing the belt location.
  Adding a steel shaft to tighten the belt

## Slide 20: Future Improvements
Use a handler to change the belt location

## Slide 21: Future Improvements
Use better pulleys and bearings.
Select better material for cons.

## Slide 22: Challenges

## Slide 23: Acknowledgment
Prince Mohammed bin Fahad University has prepared us to be qualified engineers who can work in various fields in industry, make changes effectively and contribute to the success of our country in future.
We would like to thank Dr. Ragurahman Kannan for his expert advice and encouragement throughout this difficult project, as well as Dr. Nader AlSawalhi for his valuable directions and motivating words.
We would also like to thank Saudi Aramco Eng. Ahmad AlShammari for his support as a consultant in our project issues

## Slide 24: Thank you for your Listening