## Slide 1: Design of Portable Solar Cooler
Abdullah ALDakhil 201500075
Mohammad Alhuneyn 201400282
Abdullah ALFares 200900761
Salah ALMutairi 201301812
Omar ALDossary 201101301
Advisor: Dr. MOHAME ELMEHDI SALEH
Co. advisor: Dr. ESAM JASSIM

## Slide 2: Presentation Content:
Project definition
Objectives
Background
Motivation
Design constrain
Design methodology
Specifications
Theoretical calculations and design
Assembly – exploded CAD model
Up to date progress

## Slide 3: Project Definition
Portable Solar Cooler as the names suggest is new concept of a domestic appliance intended maintain a desired temperature where electricity is not available.
Solar Cooler is an essential appliance to save the electric energy, it is basic need where the electric energy is not available, as in small towns and rural areas.

## Slide 4: Objectives
To design a proto-type of a small portable refrigerating system powered by solar cells.
To measure and maintain the low temperature inside cabin.
To apply the thermodynamics concept to design of cooling system.
To apply heat transfer concept to design cooler enclosure and select appropriate material for insulation.
To overcome the need to use a condenser and evaporator by using a thermoelectric cooler.

## Slide 5
Background
We all know from experience that heat is transferred in the direction of decreasing temperature, that is, from high-temperature mediums to low temperature ones. This heat transfer process occurs in nature without requiring any devices but the inverse would require an external device.
In the poor areas and those who need medical help and supplies the issue is not in only getting the supplies but most importantly in how to keep those supplies in the desired temperatures without being spoiled. Those areas such as the countries that suffer from poverty in Africa dose not have electricity and this is where the importance of a portable solar cooler comes.

## Slide 6
Motivation
In the last years environmental concerns have developed to became a major crises. One of that concerns is to seek for echo friendly energy sources.
solar energy and use it to supply our portable cooler.
The portable cooler idea came for those who is in need for necessary supplies like medications.
In travel, camping, or in the desert, the portable cooler is a fundamental tool to take as well .

## Slide 7
Design Constraints
Before the designing began, the following points should be considered:
Cooling capacity
Cooling rate
4 L of cooling chamber
Capable of maintaining the cabinet temperature from 7oC to 19oC
Cools using a battery and a solar cell as electricity suppliers
Combat and easy to transfer
Weight: 3-5 kg
Cooling rate capacity is calculated based on the required temperature maintained.

## Slide 8
Design Methodology:
Thermoelectric cooler works on the PELTIER thermoelectric cooling technology, which is the direct conversion of electric voltage to thermal differentials and SEE-BACK effect is vice versa.
Solar panel or solar cell which converts light energy into electrical energy is composed of P-N junctions, where electric current is produced due to the transfer of electrons.
The current stored in the battery is only used in the absence of sunlight. And when there is abundant of sunlight the solar plate is directly connected to the refrigerator

## Slide 9
Project Specifications
Design the parts of the portable solar cooler.
Construct a solar cooler which will be easily portable.
Assembling the parts of solar cooler.
Prepare prototype for study purpose.
Minimize the power consumption.
Provide proper insulation to reduce power requirement.
Using thermoelectric coolers

## Slide 10
Theoretical Calculations and Design

## Slide 11
Calculation of Mass of Air Inside Chamber:
Vchamber = 13,500 cm3
Tair = 26oC = 299.1 K

## Slide 12
Data Collected:

## Slide 13
Active Heat Load Calculations:
The active heat load is the heat released by a mass which is kept inside the cabinet during the cooling and is calculated by,

## Slide 14
Additional Calculation:
Voltage, V = 12 V
Current in TEC, ITEC = 4.6 A Current in fan, Ifan = 0.13 A
Total Power input = V*Itotal

## Slide 15
Coefficient of Performance:
Finally, the coefficient of performance using the Peltier can be numerically calculated as,

## Slide 16
Assembly-Exploded CAD First Model:

## Slide 17
Assembly-Exploded CAD Second model:

## Slide 19
Experiment Set-up:
DC power supply is used instead of solar panel instead of solar panel and a battery.
For insulation purposes, 10mm thick polystyrene foam is attached to the outer surface of the aluminum inner container.
At the bottom the PELTER is placed between a metal block and the outer bottom surface of the aluminum with thermal past on all connected surfaces and the metal block is attached and held by screws to the bottom surface of the aluminum inner container.
The metal block is screwed to a heat sink from the other end and a fan on top of the heat sink.
Additional thermal insulator were added in the sides of the metal block to prevent the hot air from going back to the cooling area and get released into the atmosphere.

## Slide 20
Testing and Correcting Errors
Chart: Time-Temperature Curve
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
Temperature, T (deg C) | 21.1 | 20.6 | 20.3 | 19.9 | 19.5 | 19.3 | 19 | 19.7 | 20.1 | 21 | 22.1 | 22.9 | 23.7 | 24.2 | 24.7 | 25.1 | 25.8 | 26.1 | 26.7 | 27.1 | 27.7 | 28.1 | 28.8 | 29.1 | 29.9 | 30.2
Chart: Cooling/Heating rate Vs Time
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
Heat Rate (J/min) | 83.3 | 50 | 66.6 | 66.6 | 33.3 | 50 | -116.5 | -66.6 | -149.8 | -183.1 | -133.2 | -133.2 | -83.3 | -83.3 | -66.6 | -116.5 | -50 | -99.9 | -66.6 | -99.9 | -66.6 | -116.5 | -50 | -133.2 | -50

## Slide 21
After Editing:

## Slide 22
Up to Date Progress

## Slide 24
Further improvement of COP can be achieved with use of increased figure in merit Peltier modules.
The efficiency of the system by improving module contact resistance, thermal interfaces and heat sinks.
Installing more modules in order to cover a greater surface area of the system and increase the cooling rate.
Testing the system in different temperature and using different fluid in the chamber such as water.
Future Recommendation

## Slide 25
In this project work a portable thermoelectric refrigeration system was fabricated and tested for the cooling purpose. The portable cooler was designed based on the principle of a thermoelectric module to create a hot side and cold side.
Conclusion