## Slide 1: Optimization of ignition timing in spark ignition engine
Group members:
Ibrahim AlAbdulhadi 201101256
Mushari Alharbi 201100959
Majed Alotaibi 201100716
Ali Al-Radhi 201101315
Abdullah Bassri 201103049
Advisor: Dr. Esam Jassim
Senior Design Project:
College of Engineering
Department of Mechanical Engineering
Spring 2016-17

## Slide 2: Outline
Introduction
Objectives
Background
Design
Testing
Time table
Challenges
Engine
Conclusion
Recommendations

## Slide 3: Introduction
Engine Specifications
Ignition timing is considered one
of the most important functions for
achieving the highest efficiency
Optimize ignition timing in spark
ignition engines and study how it
affects on the performance

## Slide 4: Objectives
Optimizing ignition timing in a spark
ignition engine
Identifying relationship between
ignition timing and exhaust emission
Radiator effectiveness in relation
to ignition timing

## Slide 5: Background
Ignition timing is crucial in the
performance of the engine
There are many factors that
influence proper ignition timing
for a given engine and a fuel
Effects of the ignition timing
on the exhaust gas

## Slide 6: Four stroke cylinder cycle
Intake stroke
Compression stroke
Power Stroke
Exhaust stroke

## Slide 7: Camshaft Angle Adjust
By changing the camshaft angle the intake of fuel and air into a piston changes thus changing the ignition time with respect to piston position, and therefor changing the performance as a hole.

## Slide 8: AutoCAD design

## Slide 9: Testing
Thermocouples to get radiator coolant temperature
i100 for measuring Ignition timing, and camshaft angle
HG-510 for exhaust gas analysis
Thermocouples
i100 Carman
HG-510

## Slide 10: Results – Part 1
BTDC | Q max (Kw) | Q actual (Kw) | Tw out predicted (C˚) | Tw out measured (C˚)
7 | 36.762 | 33.0858 | 39.522 | 45.6
10 | 28.251 | 25.426 | 38.47 | 37.2
12 | 21.639 | 19.475 | 37.66 | 34.4
Chart: Temperature of water out vs. Ignition Angle
| 7 BTDC | 10 BTDC | 12 BTDC
Tw out P. | 39.522 | 38.47 | 37.66
Tw out m. | 45.6 | 37.2 | 34.4

## Slide 11: Results – Part 2
BTDC | Co (%) | a | b | d | e | f
12 | 0.06 | 10.7745 | 4.549 | 3.4507 | 9 | 40.512
10 | 0.05 | 11.0622 | 5.1244 | 2.8756 | 9 | 41.5939
7 | 0.04 | 2.3809 | 5.6191 | 2.3809 | 9 | 42.5239
BTDC | Ø | CO2 (%) | CO (%) | H2O (%) | N2 (%)
12 | 6.2869 | 7.91 | 6 | 15.65 | 70.44
10 | 6.45479 | 8.75 | 5 | 15.36 | 70.99
7 | 6.5992 | 9.44 | 4 | 15.12 | 71.44
Chart: Ignition angle vs. Gases percentage
| 7 BTDC | 10 BTDC | 12 BTDC
CO2 (%) | 9.44 | 8.65 | 7.91
CO (%) | 4 | 5 | 6
H2O (%) | 15.12 | 15.36 | 15.65
N2 (%) | 71.44 | 70.99 | 71.44

## Slide 12: Time Table
Week 2
Week 3
Week 5
Week 6
Week 12
Week 12
Week 13
Week 14-16
Wee k 14-16
Task 1
Feb 12
Task 2
Feb 19
Task 3
Mar 5
Task 4
Mar 12
Task 5
Apr 23
Task 7
Apr 30
Task 8
7 May
Task 9
10 May
Sun 12/2/17
Thu 16/2/17
Task 1:Group Formation
Sun 19/2/17
Thu 23/2/17
Task 2: Gantt Chart
Sun 12/3/17
Thu 16/3/17
Task 4:Engine & Sensors Purchase
Sun 26/4/17
Thu 30/4/17
Task 6:Testing & Chapter 4
Sun 23/4/17
Thu 23/3/17
Task 5:Midterm Presentation
Thu 30/4/17
Thu 4/5/17
Task 7: Chapter 5&6
Sun 5/3/17
Thu 9/3/17
Task 3:Chapter 1&2
Mon 29/5/17
Thu 1/6/17
Task 8: Final Report Completion
Mon 29/5/17
Mon 29/5/17
Task 9: Final Presentation
Task 6
Apr 26

## Slide 13: Challenges
Locating engine
Local market
  Doesn't support research services
  Lacking of skilled operators/ workforce
Overweight of the engine

## Slide 14: Challenges
Assembling the engine in the frame
Electrical connection
Unavailability of some parts- Gas sensor

## Slide 15: Engine

## Slide 16: Conclusion
Ignition timing affects many variables
The optimum angle
Temperature of water out
Exhaust gas emissions

## Slide 17: Recommendations
Buying a new engine to get in order to decrease efficiency losses
Using various types of biofuel and compare results
Availability of sensors (torque sensor)
The usage of more advance technology such as the computer simulated dashboard, and LAB simulated experiments

## Slide 18: Thank you for your attention