## Slide 1: Design of a pilot-scale water hammer system
Presented By: Team 1
Mohammed Alabdullah 200700514
Sadiq Alabdullah 201300497
Mohammed AlSamadani 201400295
Mohammed Owaiwi 201302413
Advisor:
Dr. Essam Jassim

## Slide 2
Objectives
Background and History
Motivation and Relevance
Typical Cases of Damage
Design constrains
Engineering Standers and Design Specifications
Theoretical Calculations
Solidworks Design
System Testing and Analysis
Future Work and Recommendations
Short video
Content

## Slide 3
Objectives
To design a test stand for water hammer system
To design and select the required pipes and pump
To select the flow type required valve.
To measure the increases in pressure in the pipes due to the pressure wave.
To investigate the effect of piping length and design.
To investigate the effect of the shutting off time of the flow.

## Slide 4: Background and History
Definition of the water hammer.
Causes and consequences of water hammer.
Brief history of Water hammer.
Joukowsky equation of water hammer.

## Slide 5
Motivation and Relevance
Water hammer is a dangerous phenomenon which can result in remarkable damages to pipes
Need for adopting strategic interventions aimed at checking the problem
Need to be aware of the situation under which water hammer occur

## Slide 6
Pipe damage in
power station Okigawa
Burst pipe in power
sation Big Creek #3, USA
Pump damage in Azambuja
Portugal
Some typical CASES OF DAMAGE

## Slide 7
Design Constraints
Following are design constraints:
Material Elastic properties. (pipes, valves,..etc).
Fluid temperature effects.
Fluid velocity versus surge pressure.
Valve closure timing.
Lose of containment (regarding of fluid leakage)
Safety concerns.

## Slide 8
Engineering standards & Design specification
Pipe:
Outer diameter of pipe = 50.8 mm
Thickness of pipe = 3 mm
Length diameter of pipe = 2.4 m
Hoses:
Nominal Size = 50.8 mm
Length = 3 m, 1.5m, 1m
Valves:
Size = 3 EA 2 Inches size
Pressure gauges = 200 psi capacity
Total Volume of the system=10 Liters
Standards used:
PVC Inert in Fittings ASTM D2609
PVC Joining ASTM D2564
PVC Pipes ASTM D1785
Acrylic Pipe ASTM D638
Pressure gauges ASME B40.100

## Slide 9: Engineering standards & Design specification (cont’d)
Pump selection:
2 Horse power
2” outlet and inlet.
Q=100 – 500 l/min

## Slide 10: Theoretical calculation
The pressure rise due to water hammer depends upon:
The velocity of the flow of water in pipe,
The length of pipe,
Time taken to close the valve,
Elastic properties of the material of the pipe.
Design of the piping

## Slide 11
Theoretical calculation(cont’d)
Magnitude of water hammer pressure is given as:
Where: = Change in pressure
= Fluid Density
U = Change in fluid velocity
C = sonic Velocity in a pipe
Sonic velocity is the speed of sound in a pipe and given as:
Slow valve closure

## Slide 12
Solidworks model

## Slide 13
fabrication

## Slide 14: fabrication

## Slide 15: System Testing and Analysis
Hose length | Pressure | 
 | Upstream | Downstream
1 | 56 | 36.4
1.5 | 34 | 32.3
3 | 15 | 11.5
Hose length | Pressure | 
 | Upstream | Downstream
1 | 30 | 25
1.5 | 24 | 21.3
3 | 12 | 14.5

## Slide 16: System Testing and Analysis
Hose length | Pressure | 
 | Upstream | Downstream
3m no loop | 15 | 11.5
3m 1 loop | 5 | 18.6
Hose length | Pressure | 
 | upstream | Downstream
3m no loop | 12 | 14.5
3m 1 loop | 24 | 21.3

## Slide 17: System Testing and Analysis
Time | Pressure
0.5 | 40.1
1 | 31
2 | 10

## Slide 18
Future work & Recommendations
More testing points
More loops
Different hose diameter
Rigid system with fixed pipes
Adding water tower
Using different types of valves

## Slide 19: Video

## Slide 20
references
Menabrea, L. F., 1885, ‘‘Note sur les effects de choc de l’eau dans les conduites,’’ C. R. Hebd. Seances Acad. Sci. 47, July–Dec., pp. 221–224.
Michaud, J., 1878, ‘‘Coups de be´lier dans les conduites. E´tude des moyens employe´s pour en atteneur les effects,’’ Bull. Soc. Vaudoise Ing. Arch. 4~3,4!, pp. 56–64, 65–77.
Weston, E. B., 1885, ‘‘Description of Some Experiments Made on the Providence, RI Water Works to Ascertain the Force of Water Ram in Pipes,’’ Trans. Am. Soc. Civ. Eng. 14, p. 238.
Carpenter, R. C., 1893, ‘‘Experiments on Waterhammer,’’ Trans. ASME, 15.
Frizell, J. P., 1898, ‘‘Pressures Resulting from Changes of Velocity of Water in Pipes,’’ Trans. Am. Soc. Civ. Eng. 39, pp. 1–18.
Joukowski, N. E., 1898, ‘‘Memoirs of the Imperial Academy Society of St. Petersburg,’’ 9~5! ~Russian translated by O Simin 1904!, Proc. Amer. Water Works Assoc. 24, pp. 341–424.
Ord, S., C. (2006). Water hammer-Do we need to protect against It?: How to predict it and prevent it damaging pipelines and equipment. IChemE. Retrieved from https://www.icheme.org/communities/subject_groups/safety%20and%20loss%20prevention/resources/hazards%20archive/~/media/Documents/Subject%20Groups/Safety_Loss_Prevention/Hazards%20Archive/XIX/XIX-Paper-14.pdf
Subani, N., & Amin, N. (2015). Analysis of Water Hammer with Different Closing Valve Laws on Transient Flow of Hydrogen-Natural Gas Mixture. Journal of Loss Prevention in the Process Industries
Wang et al. (2014). Water hammer assessment techniques for water distribution systems. Procedia Engineering 70, 1717-1725.
Choon et al. (2012). Investigation of water hammer effect through pipeline system. International Journal on Advanced Science Engineering Information Technology 2(3), 2088-5334